## Slide 1
FAR 139.329 Ground Vehicle Operations on Movement & Safety Areas
Tug and Tow/Run-Taxi Operators
Revised 6/2022

## Slide 2: Could this happen to you?
Springfield-Branson Airport, June 27, 2018
(click here to play video)

## Slide 3: Airport Movement Area Initial Training for Tug and Tow/Run Taxi Operators - Outline
Topics
  FAR 139/FAA and WCAA Letter of Agreement and Movement Areas
  Prerequisites to Operate a Vehicle on Movement Areas
  Airport Movement and Non-Movement Areas
  Low Visibility/SMGCS
  Runway Protected Areas
  Airfield Markings, Lights, and Signs
  Situational Awareness
  Airfield Safety and Runway Incursion Awareness/Prevention
  Airfield Radio Communications and Procedures
  Airfield Familiarization
  Ground Run-up Enclosure (GRE) Operations
  Evaluations
  Airfield Safety Exam
  Map Test

## Slide 4: Why are we here? FAR 139
  FAR 139 states that airport operators (Wayne County Airport Authority) shall control access to the airport’s
  movement area.
    This includes tug and tow operations as well as aircraft taxiing without the intent of flight.
  It also states that training shall be conducted and completed before individuals can access the
  movement area.
    Once the initial training is complete, recurrent training must be completed at least once every 12
    consecutive calendar months.
    The training curriculum for initial and recurrent training must include at least the following areas.
      Airport familiarization, including airport marking, lighting, and signs system.
      Procedures for access to, and operations in, movement areas and safety area.
      Airport communications, including radio communication between the air traffic control tower
      and personnel, and procedures for reporting unsafe airport conditions.

## Slide 5: Why are we here? Letter of Agreement (LOA) – Between the FAA and the Wayne County Airport Authority
  States that tug and tow/run taxi personnel must receive prior approval from ATC before accessing the AMA.
  The LOA states that tow and tug/run-taxi operators shall use the following communications procedures,
  structure, and phraseology when communicating with DTW ATC:
    On initial contact state:
      Who the operator is calling “Metro Ground”
      Operator’s call sign. (wait for controller response)
      Operator’s location.
      Operator’s destination or request, if applicable purpose of request.
      Keep all transmissions short, concise, and to the point.
      Read back verbatim all runway hold short instructions and all other controller instructions
      and include the vehicle’s call sign.

## Slide 6: Why are we here? Letter of Agreement – Between the FAA and the Wayne County Airport Authority
The LOA also states which taxiways tug and tow operations may occur.

## Slide 7: What are the Prerequisites to Operate on the Movement Area?
Airport Authority
DTW 00/00
Doe,
John
Operators must have:
a valid and current state-issued driver’s license, not suspended or revoked.
a valid and current airport security badge with the AMA icon on it issued by Airport Security, not suspended or revoked.
a valid reason for entering the movement area (must be related to work duties that have to be performed on the movement area).
a current training date (no more than 12 consecutive calendar months since date of previous training)

## Slide 8: What are the Components of the Non-Movement Area?
            Taxilanes – Provide routes for aircraft between ramps/aprons
            and movement areas. They are ONLY found in Non-Movement Areas.
            Ramps (Aprons) – Used for aircraft parking, loading, and servicing.
            De-Ice Pads – Used for the deicing of aircraft prior to takeoff.
Aircraft and vehicle movements are
NOT controlled by FAA
Air Traffic Control Tower (ATCT).
Permission from ATCT to enter non-movement areas is not
required.

## Slide 9: What are the Components of the Movement Area?
            Runways – Are protected areas used for aircraft taking off and landing.
            Taxiways – Provide routes between Non-Movement Areas and runways. They are like taxilanes but are found ONLY on Movement Areas.
Aircraft and vehicle movements
ARE controlled by FAA
Air Traffic Control Tower (ATCT)
Entering a Movement Area or a Runway without ATCT permission, will result in the person being charged with a
SURFACE INCIDENT or
RUNWAY INCURSION.

## Slide 10: SMGCS Plan
What does “SMGCS” stand for:
Surface Movement Guidance and Control System
What is the SMGCS Plan:
A low visibility taxi plan required for any airport which has scheduled air carrier takeoff or landing operations with less than 1,200 feet runway visual range (RVR) visibility conditions.
This plan affects flight crew, tug/tow, run/taxi, and vehicle operators.
It reduces the potential for runway incursions by improved signage, lighting and markings.
Movement Area access is limited to those supporting the plan. ALL tug and tow/run taxi operations are suspended.

## Slide 11: Runway Protection Areas
        Runway Safety Areas (RSA)
        Runway Protection Zone (RPZ)
        Instrument Landing System (ILS)

## Slide 12: Runway Safety Area (RSA)
The RSA is an invisible imaginary surface but is made apparent by signs and markings, in most cases lights too.
DO NOT CROSS WITHOUT ATC PERMISSION

## Slide 13: What does the RSA look like?
Runway Holding Position Signs and markings are always located at taxiways prior to entering a Runway Safety Area.
22L-4R
Edge
of
RSA
22L-4R
22L-4R
22L-4R
500’
22L
4R
1000’
4R-22L
4R-22L
RSA Dimensions
Length: Runway Length + 1000’ beyond each threshold
Width: 500’ centered over runway

## Slide 14: Instrument Landing System (ILS)
The ILS is an invisible imaginary surface but is made apparent by signs and markings.
DO NOT CROSS WITHOUT ATC PERMISSION

## Slide 15: What do you need to know about the ILS?
The ILS is used to assist aircraft in landing.
An aircraft can use ILS signals to land at any time, regardless of weather conditions. Good weather is NOT an indication that an ILS is not being used.
Vehicles, aircraft, equipment, or other objects in an ILS critical area could interfere with an ILS signal and pose a safety hazard to aircraft using the ILS.
Operators have no way of knowing when an aircraft is using an ILS.

## Slide 16: Runway Protection Zone (RPZ)
The RPZ is an invisible imaginary surface but is made apparent by signs and markings.
DO NOT CROSS WITHOUT ATC PERMISSION

## Slide 17: What is the RPZ?
RPZ: Do not penetrate this imaginary surface without ATCT clearance
An RPZ is an area off the runway end used to help protect people and property under the approach to the runway. The RPZ is trapezoidal in shape and centered on the extended runway centerline.
The approach above the RPZ is protected by an imaginary surface. The surface starts at ground level 200 feet from the threshold of the runway and slopes up and away from the runway.
The surface cannot be penetrated by aircraft, vehicles, or other objects without ATC permission.

## Slide 18: Where at DTW should I be concerned about an RPZ?
22L
Overhead View
Aircraft under tow or taxi must obtain permission from ATC before passing the signs and crossing the hold bars
Rwy 22L RPZ
200’
K
Side View
K
Nothing can penetrate the RPZ until permission is given by ATC

## Slide 19: Overview of RSAs and ILSs
Runway Safety Areas
ILS Critical Areas

## Slide 20: Airfield Markings
            Runway Holding Positions
            Movement/Non-movement
            ILS Critical Area Holding Position
            Taxiways
            Geographic Position Markings
            Runway

## Slide 21: Runway Holding Position Marking
Hold Short on This Side
Identifies the position at which pilots and vehicle operators must hold short of a runway safety area or other protected area.
You must at the holding position until given permission to cross by ATC!
Which side do you hold short of?

## Slide 22: Movement/Non-Movement Boundary Marking
Non-movement side
Marks the boundary between movement and non-movement areas.
Which side is the non-movement side?

## Slide 23: ILS Critical Area Holding Position Marking
Protects the area through which ILS signals are transmitted.
Vehicles and aircraft in the ILS critical area can interfere with the signals.

## Slide 24: Taxiway Edge Line Marking
Aircraft – OK both sides
Aircraft - yes
Aircraft - no
Continuous Taxiway Edge
No useable pavement for aircraft on the other side of the line.
Dashed Taxiway Edge
Alt. Dashed Taxiway Edge
Dashed - aircraft can use pavement on both sides of the line.

## Slide 25: OOPS!
Taxiway Edge Marking
Photo on Airliners.net by SkyArts Aviation Photography

## Slide 26: Taxiway Holding Position Marking
Can be seen approaching a taxiway intersection where ATC normally holds aircraft short of a taxiway intersection.
Allows adequate wingtip clearance for aircraft passing through the intersection.
Do not confuse this marking with movement/non-movement area boundary markings OR dashed taxiway edge lines.

## Slide 27: Taxiway Centerline Marking
Provides pilots a visual cue to permit taxiing along a designated path.

## Slide 28: Enhanced Taxiway Centerline Marking
Gives warning that a runway hold short position marking is located ahead. Especially helpful during conditions of reduced visibility.
Be prepared to at the runway hold short position until cleared onto or across the runway by ATC.

## Slide 29: Geographic Position Markings - Overview
Spots 1-8
22L Pad and
North Terminal
Spots 1N-4N
Spots 1S-4S
McNamara Terminal

## Slide 30: Geographic Position Marking – North Terminal
Spots are “shorthand” for giving locations on selected taxilanes.
Two spots are near the 22L deice pad.
Four spots are parallel to and west of the North Terminal (Taxilane E).
Two spots are at the north end of the North Terminal.
Each spot at the North Terminal is a black number on yellow background.

## Slide 31: Geographic Position Marking Locations at the North Terminal
Single-digit numbers, numbered south to north.
22L Deice Pad
North Terminal

## Slide 32: Geographic Position Marking – McNamara Terminal
Spots are “shorthand” for giving locations on selected taxilanes.
Combination of a number and letter, numbered east to west.

## Slide 33: Geographic Position Marking Locations at the McNamara Terminal
North End
4N
3N
Taxilane Q
Taxilane U-9
2N
1N
Taxilane U-8
Taxilane U-7

## Slide 34: Geographic Position Marking Locations at the McNamara Terminal
South End
4S
3S
2S
1S
Taxilane Q
Taxilane U-9
Taxilane J-8
Taxilane J-7

## Slide 35: Runway Markings
Runway markings come in a variety of sizes and shapes. They are all WHITE. If you are seeing white markings, YOU ENTERED A RUNWAY. If you did NOT receive permission from ATCT to be on the runway, EXIT IMMEDIATELY, call ATCT, and tell them where you are!

## Slide 36: Airfield Markings - Review
Runway Holding Position
Movement/Non-Movement
Area Boundary
Taxiway Holding Position
ILS Critical Area
Holding Position
Continuous Taxiway Edge
Dashed Taxiway Edge
Dashed Taxiway Edge
Taxiway Centerline
Enhanced Taxiway Centerline

## Slide 37: Airfield Lighting
            Taxiway Lights
            Runway Lights
            Runway Guard Lights
            Runway Status Light System

## Slide 38: Taxiway Edge Lights
Taxiway edge lights identify the edge of the usable taxiway surface at night and during periods of low visibility.
Taxiway edge lighting is blue.

## Slide 39: Taxiway Centerline Lights
Taxiway centerline lights are green.
They are placed on selected taxiways to assist pilots with taxiing at night and during periods of reduced visibility.
They are also placed on Rwy 9L/27R between 4R/22L and 3L/21R, since that section of runway is normally used as a taxiway.

## Slide 40: Runway Edge Lights
Runway edge lights Identify the edge of the usable runway surface at night and during periods of low visibility.
Runway edge lights are clear (or white), except for the last 2000’ of certain runways. The half of the lights facing the pilot are amber.

## Slide 41: Runway Centerline Lights
Runway centerline lights give pilots a visual reference for the centerline.
They are clear (or white), except for the last 3000’ of certain runways.
Starting at 3000’ remaining, the lights are alternating red and white.
Starting at 1000’ remaining, the lights are all red.

## Slide 42: Runway Threshold Lights
Used to mark the end of useable runway pavement for aircraft.
Arranged in two sets of four lights.
Lights are split into two colors:
Green face away from runway
Red face towards the runway

## Slide 43: Runway Guard Lights
Elevated Runway Guard Lights
Used to identify the holding position for a runway especially at night and during periods of low visibility.
Elevated runway guard lights are amber.

## Slide 44: Runway Guard Lights
In-Pavement Runway Guard Lights
In-pavement runway guard lights are co-located with runway hold bars, above-ground runway guard lights, and hold position signs. These lights are yellow.
At this time, these lights are only installed at certain taxiway intersections at DTW.

## Slide 45: Runway Guard Lights
In-Pavement and Elevated Runway Guard Lights at Night
In-Pavement
Elevated

## Slide 46: Runway Status Light System
Provides visual signal to pilots and vehicle operators that it is unsafe to enter, cross, or begin takeoff on a runway.
Designed to reduce the number of runway incursions without interfering with normal and safe airport operations
Automatic system that gives an added layer of safety for the runway environment
Gives warning of a potential conflict on a runway between aircraft and/or vehicles
Indicates runway status only
Does not give or imply clearance
to cross a runway

## Slide 47: Runway Status Light System
DO NOT PROCEED after the lights go out until ATC specifically tells you to.
If ATC tells you to proceed and the lights are “on”, DO NOT PROCEED – HOLD YOUR POSITION.
Call ATC and tell them “[call sign] is holding short of Runway XX at Taxiway X due to red lights.”
If ATC tells you to proceed and the lights come on after you cross the hold short position. CLEAR THE RUNWAY IMMEDIATELY AND CALL ATC.

## Slide 48: Runway Status Light System
Takeoff Hold Lights (THLs)
THLs tell pilots to STOP because of a potential conflict further down the runway.
No action is required by vehicle operators, but know they are there.

## Slide 49: Runway Stop Bar Lights
Can be placed at select runway/runway and taxiway/runway intersections to highlight potentially hazardous runway hold positions.
Lights are uni-directional, steady red color (do not flash).
There are two different types.
In-pavement located at all locations
Elevated located at certain locations

## Slide 50: Runway Stop Bar Lights – Locations
27R
21R
22L
There are three locations to be concerned with
Two are located on Runway 27R:
One at Runway 21R
The other at Runway 22L
The third one is located on Taxiway B on the south
of Runway 27R

## Slide 51: Airfield Signage
            Taxiway Location
            Taxiway Directional
            Surface Painted

## Slide 52: Taxiway Location Signage
Identifies the taxiway on which the aircraft or vehicle is located.
The inscription is yellow with a black background.

## Slide 53: Taxiway Directional Signage
Identifies the direction(s) in which a taxiway goes.
The inscription is black with a yellow background.
Taxiway location and directional signs are often co-located together in a sign array.

## Slide 54: Taxiway Signage Arrays
Black sign indicates the taxiway/taxilane that you are on
Arrows on yellow signs point in the direction of a turn ahead

## Slide 55: Surface Painted Signage
Signs can also be painted on the pavement
They look just like their physical counterparts
Surface Painted Runway
Holding Position
Surface Painted
Taxiway Location
Surface Painted
Taxiway Directional

## Slide 56: What are the 7 indications that you’re approaching a runway hold position? (some are not at all intersections)
1
Mandatory Hold Position Sign
2
Elevated Runway Guard Lights
3
Runway Holding Position Bar
4
Surface Painted Hold Position Sign
5
Enhanced Taxiway Centerline
6
In-Pavement Runway Guard Lights
7
Runway Status Lights
1
2
3
5
4
6
7

## Slide 57: Radio Communication and Procedures

## Slide 58: Radio Communication the Basics
Always use standard FAA ATCT phraseology
Know what you are going to say before you say it
Listen to radio traffic before transmitting.
Do not interrupt other radio transmissions
Listen closely to all instructions
Never make assumptions. If you are not sure of your instructions, then ask ATCT to say it again
Read back all instructions, especially Hold Short instructions and other runway instructions
Always monitor ground control while in the movement area
Make sure equipment is working properly before entering the movement area
IMPORTANT: if you need permission to enter or drive on the movement area, do not proceed without ATCT instructions.
If you cannot contact a controller after repeated attempts:
  Lack of response from ATCT does not imply permission to proceed.

## Slide 59: Radio Communication the Basics
How can listening to the aviation (“FAA”) radio help me?
SITUATIONAL AWARENESS
  Let's you hear where aircraft are and where they’re going.
  Helps you form a “mental map” of what’s going on.
What am I listening for?
  Pilots/ vehicle operators giving their location and requesting instructions to go somewhere.
  Controllers telling pilots/vehicle operators what route or routes to take.
  Potential conflicts between you and aircraft/vehicles.

## Slide 60: FAA Phraseology
Roger – I have received all of your transmission. Not to be used to answer “Yes” to a question.
Wilco – I have received your transmission and I will comply.
Affirmative – Yes
Negative – No
Acknowledge – Confirm that you have received my message.
Read back – Repeat message.
Say Again – Request a repeat of instructions.
Stand By – Wait, controller is busy with other tasks. May require waiting several minutes.

## Slide 61: FAA Phraseology
Go Ahead – State your request.
Proceed – Authorization to begin/continue driving
Advise intentions – What do you plan to do.
Without Delay – Proceed with approved instructions immediately.
Expedite – Comply promptly with instruction.
Immediately – NOW!
Unable – Indicates inability to comply.
Hold – Stay in place, do not move.
Hold Short – Hold short of a specific point as instructed by the controller. Often at Runway/Taxiway intersections

## Slide 62: Phonetics
A - Alpha
B - Bravo
C - Charlie
D - Delta
E - Echo
F - Foxtrot
G - Golf
H - Hotel
I - India
J - Juliet
K - Kilo
L - Lima
M - Mike
N - November
O - Oscar
P - Papa
Q - Quebec
R - Romeo
S - Sierra
T - Tango
U - Uniform
V - Victor
W - Whiskey
X - X-ray
Y - Yankee
Z - Zulu
Letters

## Slide 63: What are the Radio Frequencies at DTW
Ground Control Frequencies:
  121.8 (North)West Ground
  119.45 (North) East Ground
  119.25 Southeast Ground
  132.725 Southwest Ground
  ATIS (Automated Terminal Information System)
  133.675 ATIS Arrivals- Automated Terminal Information System
  118.125 ATIS Departures

## Slide 64: A Map View of the Radio Frequencies

## Slide 65: North Terminal – United Gates
Movement/Non-Movement Boundary Line
Taxilane E
Gate D6
Gate D4
Gate D2
Gate D1
Gate D3 & 3A
Gate D5 & 5A
Gate D8
Gate D9
Gate D10
Due to Movement/Non-Movement Boundary line, gates D4, D6 will need to contact FAA ground control when “Pushing Back”

## Slide 66: North Terminal – American Gates
Taxiway K
Movement/Non-Movement Boundary Line
Zipper Road
Gate D32
Gate D30
Gate D28
Taxilane E
Gate D25
Gate D26
Due to Movement/Non-Movement Boundary line, gates D30 & D32 will need to contact FAA ground control when “Pushing Back”

## Slide 67: What’s a Read Back? AND What do you need to know about them?
What is a Read Back?
  Repeating an ATCT instruction verbatim.
You will hear pilots and drivers reading back instructions.
Readbacks give you a second chance to hear a controller’s instructions and help you maintain “situational awareness.”
You are required to read back ALL runway instructions, especially HOLD SHORT instructions.
Other Read Back instructions:
  To drive requested routes.
  To change frequencies.
  That are changes to previous Instructions.

## Slide 68: What do ATCT Controllers expect to hear when you make initial contact with them?
Who you are calling (Metro Ground)
Who you are (your call sign)
Where you are (your location)
Where are you going

## Slide 69: Communication Example #1 – STS
Who you are calling and Who you are:
“Metro Ground Air Canada Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“Air Canada Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“Air Canada Maintenance, is at Gate D-4, would like to push and reposition to CDF Hardstand Spot 4”
ATCT response:
“Air Canada Maintenance push approved, call back with reposition”
Your Response:
“Air Canada Maintenance, push approved, will call back with reposition”
(continue)

## Slide 70: Communication Example #1 (Continued) – STS
You are pushed back on Taxiway K and ready to tow to CDF Hardstand Spot 4:
Who you are calling and Who you are:
“Metro Ground Air Canada Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“Air Canada Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“Air Canada Maintenance, has pushed off D-4 and is ready to reposition to CDF Hardstand Spot 4”
ATCT response:
“Air Canada Maintenance proceed K, E-2 to CDF Hardstand Spot 4”
Your Response:
“ Air Canada Maintenance, proceeding K, E-2 to CDF Hardstand Spot 4”

## Slide 71: Communication Example #2 – STS
Who you are calling and Who you are:
“Metro Ground United Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“United Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“United Maintenance, is at D-6, would like to push and reposition to CDF Hardstand Spot 4”
ATCT response:
“United Maintenance push approved, call back with reposition”
Your Response:
“United Maintenance, push approved, will call back with reposition”
(continue)

## Slide 72: Communication Example #2 (Continued) – STS
You are pushed back on Taxiway K and ready to tow to CDF Hardstand Spot 4:
Who you are calling and Who you are:
“Metro Ground United Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“United Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“United Maintenance, has pushed D-6 and is ready to reposition to CDF Hardstand Spot 4”
ATCT response:
“United Maintenance proceed K, E-2, to CDF Hardstand Spot 4”
Your Response:
“United Maintenance, proceeding K, E-2 to CDF Hardstand Spot 4”

## Slide 73: Communication Example #3 – STS
Who you are calling and Who you are:
“Metro Ground United Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“United Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“United Maintenance, is at D-4, would like to push and reposition to Berry Hardstand Spot 5”
ATCT response:
“United Maintenance push approved, call back with reposition”
Your Response:
“United Maintenance, push approved, will call back with reposition”
(continue)

## Slide 74: Communication Example #3 (Continued) – STS
You are pushed back on Taxiway K and ready to tow to Berry Hardstand Spot 5:
Who you are calling and Who you are:
“Metro Ground United Maintenance”
Pause & wait for acknowledgement from ATCT:
ATCT response:
“United Maintenance Metro Ground”
Who are you, Where are you, and Where are you going (Request):
“United Maintenance, has pushed off D-4 and is ready to reposition to Berry Hardstand Spot 5”
ATCT response:
“United Maintenance proceed K to Berry Hardstand Spot 5”
Your Response:
“United Maintenance, proceeding K to Berry Hardstand Spot 5”

## Slide 75: What to do when you lose radio communication
First stop and hold your location.
Lack of response or direction does not imply permission.
Attempt to resolve the issue.
If you are unable to resolve the issue, turn your vehicle/aircraft towards the Tower, flash your lights, and follow light gun signals.
If the edge lights for the runway or taxiway you are on start flashing, the ATCT is attempting to contact you. Call them on the radio! If your radio is not working, turn your vehicle towards the ATCT, flash your lights, and follow light gun signals.
If all else fails, contact Airfield Operations at 734-942-3685. They will give you direction and if necessary, send a follow me vehicle to assist.

## Slide 76: Understanding Light Gun Signals
COLOR AND TYPE OF SIGNAL
Steady Green
Steady Red
Flashing Red
Alternating Green/Red
Flashing White
What is the tower telling you to do
Cleared to cross, proceed or go
Stop
Clear the taxiway or runway
Exercise extreme caution
Return to starting point on airport

## Slide 77: Runway Incursion Awareness and Airfield Safety

## Slide 78: What is the FAAs Definition of a Surface Incident?
“Any event where unauthorized movement occurs
within the movement area
or an occurrence in the movement area
associated with the operation of an aircraft
that affects or could affect the safety of flight.”

## Slide 79: What is the FAAs Definition of a Runway Incursion?
“Any occurrence at an airport
involving the incorrect presence
of an aircraft, vehicle or person
on the protected area of a surface designated for the landing and take-off
of aircraft.”

## Slide 80
D
Little or no risk of collision
C
Ample time and distance to avoid collision
The above scenarios are all classified as runway incursions, but with different severity codes. In each case, the vehicle has penetrated the RUNWAY SAFETY AREA (crossed the hold position).
B
Significant potential for collision
A
Barely avoid collision
Runway Incursion Severity Categories

## Slide 81: What is a Hot Spot and Where are they Located?
A “hot spot” is a location on the movement area with a high risk of collision or runway incursion, and where greater attention by pilots and drivers is necessary.
HS 1:
27R-9L @ 21R-3L (note runway stop bar lights

## Slide 82: Situational Awareness
Defined as “knowing what is going on so you can figure out what to do.”
Can be broken down with answers to the following questions:
  What is happening?
  Why is it happening?
  What could happen next?
  What am I going to do about it?
Another way to think of situational awareness while on the airfield:
  Being aware of one's surroundings…
  Identifying potential threats and dangerous situations…
  And doing something about them.

## Slide 83: What Factors can Cause you to Lose Situational Awareness?
  Complacency.
  Fixation on tasks.
  Pressure to hurry up and complete a task.
  Personal problems or other non-work events and situations that are on your mind.
What do all of these factors have in common?
They are DISTRACTIONS

## Slide 84: 3 Types of Distractions
Visual – Distractions that take your eyes off your surroundings.
Physical – Distractions that take your hands off the steering wheel (if you are driving) or off the equipment you are operating.
Mental – Distractions that take your mind off what you are doing or where you are.

## Slide 85: Here are some examples of visual distractions
Fog
Rain/Snow
Darkness/Glare
Obscured Pavement Markings
Obscured Lights and Signs

## Slide 86: What are the Consequences of a Runway Incursion?
The individual’s DTW Airport ID badge is immediately confiscated by WCAA.
The individual will not be allowed to re-enter the Airport Movement Area until the CEO receives a letter from the individual’s supervisor indicating that the individual has been counseled and has received recurrent company training.
The individual’s DTW Airport ID badge will not be returned until ground vehicle training and testing is conducted by the Airfield Operations Department.
Other discipline may be issued in accordance with individual company rules.

## Slide 87: Consequences of a Runway Incursion
The driver of this pickup truck, which was at the approach end of an open runway, saw a 747 on final approach.
He jumped out of the vehicle and ran.
The pilot reported feeling a “slight shudder” in the main gear just before landing.

## Slide 88: Consequences of a Runway Incursion
Two Boeing 747 jumbo jets collided head-on at the airport on Tenerife Island in 1977.
Because of fog, missed communications, and one pilot’s overconfidence and loss of situational awareness, one of the B-747's started its takeoff roll while the other was on the runway.
In the resulting collision, 583 people died.
For more details, Google “The True Story Behind the Deadliest Air Disaster of All Time”.

## Slide 89: Best Practices for Airfield Safety and Runway Incursion Prevention
Review and understand airfield signage and markings.
Know the Airport Layout and have a copy of the movement map out and available.
Follow established procedures.
Never make assumptions while operating in the movement area.
Use proper radio
Read back all instructions verbatim.
ASK QUESTIONS IF THINGS “JUST DON’T SEEM RIGHT!”

## Slide 90: Airfield Familiarization
Runways
Taxiway and Taxilanes
Fire Stations
Deicing Pads
RON Parking Locations

## Slide 91: Northeast/Southwest Runways
4R
22L

## Slide 92: East/West Runways
9L
27R

## Slide 93: Taxiway Y
Y
Taxiway

## Slide 94: Taxiway Y
Y
Y-5
Y-7
Y-9
Y-10
NOTE: K-5, K-7, and K-9 are in line with their Y counterparts. There is no K-10.

## Slide 95: Taxiway R
Taxiway
R

## Slide 96: Taxiway R
R

## Slide 97: Taxiway K
Taxiway
K

## Slide 98: Taxiway K
K
K-5
K-6
K-7
K-8
K-9
NOTE: Y-5/Z-5, Y-7/Z-7, and Y-9 are directly opposite from their K counterparts. There is no K-10.

## Slide 99: Taxiway B
B
Taxiway

## Slide 100: Taxiway B
B

## Slide 101: Taxiways F, G, and H
F
Taxiway
Taxiway
G
H
Taxiway

## Slide 102: Taxiways F, G, and H
F
G
H-1
H-2
H
RON Parking
&
CDF
F
22L De-Ice
Pad
H-3

## Slide 103: Taxilane E
E
Taxilane

## Slide 104: Taxilane E
E-8
E-7
E
E-2
22L De-Ice
Pad
RON Parking
&
CDF
F
E-3
E-3

## Slide 105: Taxiway V
V
Taxiway

## Slide 106: Taxiway V
V

## Slide 107: Deice Pads
Central Deice Facility
CDF
22L
22L
22L De-Ice Pad

## Slide 108: Ground Run-Up Enclosure (GRE)
GRE

## Slide 109: Overview RON Spot Parking

## Slide 110: Berry RON Parking
1
2
3
4
5
Hardstand Parking Spot Aircraft Sizes
Spots 1-3 and 5: A321 and Below
Spot 4: E-195 and Below

## Slide 111: Central Deicing Facility (CDF) RON Parking

## Slide 112: Ground Run-Up Enclosure (GRE) Operations

## Slide 113: Ground Run-Up Enclosure (GRE) Topics
Introduction
Hours of Operation and Scheduling
Aircraft Access to the GRE
Aircraft Ingress to the GRE
Run-ups within the GRE
Run-ups at Alternate Locations
Safety
Other Features

## Slide 114: Introduction
All run-ups should be conducted at the GRE
Designed to minimize the acoustic impact of ground run-ups
Lined with acoustic panels
Can accommodate aircraft up to a B747-8

## Slide 115: Introduction – Bird’s Eye View
Turnaround Point
Aircraft Lead-In Lines
Centerline w/ Nose Gear Positions
Aircraft Limit Lines

## Slide 116: Introduction – Front View
Egress Door
Wind Speed Display
H = 41’-10”
Jet Blast Deflector
Fire Extinguisher Cabinet
Acoustic Panels
Obstruction Lights
Operation Lights
Flashing Beacon

## Slide 117: Hours of Operations and Scheduling
The GRE is available for use 24 hours per day.
During snow events the GRE may be closed.
Each run-up must be pre-arranged with Airfield Operations at 734-942-3685.
First-come, first-served basis.

## Slide 118: Aircraft Access – Towed via Towbar
Aircraft towed to the GRE via a tug using a towbar shall:
Contact Airfield Operations at 734-942-3685 for an escort.
Being escorted proceed to the GRE.
Position the aircraft in the GRE safely. Use wing walkers if possible.
Notify Airfield Operations when the aircraft run-up is complete.
Wait for Airfield Operations escort you back.
Report any damage or unsafe conditions.

## Slide 119: Aircraft Ingress – Tow
B747-400, pushback operation, GRE wing walkers
Stop aircraft at designated position.

## Slide 120: Aircraft Ingress – Tow
B757-300, pushback operation
Stop aircraft at designated position.

## Slide 121: Run-ups Within the GRE
High power run-ups should be conducted in the GRE.
The GRE is designed to allow run-ups in most wind conditions.

## Slide 122: Run-ups Within the GRE
Aircraft in proper position within GRE

## Slide 123: Run-ups at Alternate Locations
If wind conditions do not allow the GRE to be used, the alternate run-up location is the apron immediately in front of the GRE.
Under no circumstances should a run-up be performed with the engines pointed toward the GRE side walls.

## Slide 124: Run-ups at Alternate Locations

## Slide 125: Run-ups at Alternate Locations
Aircraft in proper position at alternate location

## Slide 126: Run-ups at Alternate Locations
NEVER position aircraft such that the GRE will be exposed to jet blast. The side walls of the GRE are not rated for high velocity jet blast.

## Slide 127: Safety
In the event of an emergency, dial 911.

## Slide 128: Safety
EGRESS DOORS
The GRE features two egress doors.
Each door has a panic bar and an illuminated “EXIT” sign.

## Slide 129: Safety
Emergency Egress Doors provide a quick escape route.
Egress Doors

## Slide 130: Safety
FIRE EXTINGUISHERS
Both side walls have a cabinet with a dry chemical fire extinguisher.

## Slide 131: Safety
If necessary, shut off GRE’s electrical power by utilizing the “emergency power shut off” switch located outside of the control room.
Control Room

## Slide 132: Safety
Operational lights should be activated for all run-ups, 24h/day.
Flashing beacon is activated whenever lights are on.
LIGHTING

## Slide 133: Other Features
VEHICLE PARKING
Vehicles accompanying aircraft (security vehicles, miscellaneous autos, etc.) should park on the apron outside of the entrance of the facility as shown.

## Slide 134: Thank you