## Slide 1
Airfield Operations Division
Wayne County Airport Authority
FAR 139.329 Ground Vehicle Operations on Movement & Safety Areas
December 2021

## Slide 2
Wayne County Airport Authority
FAR 139.303 and 139.329 - Ground Vehicle Operations
on Movement and Safety Areas
DTW
YIP
ESA

## Slide 3
YIP
Wayne County Airport Authority
FAR 139.303 and 139.329 - Ground Vehicle Operations
on Movement and Safety Areas

## Slide 4
DTW
Wayne County Airport Authority
FAR 139.303 and 139.329 - Ground Vehicle Operations
on Movement and Safety Areas

## Slide 5
Aviation is not inherently dangerous.
But to an even greater degree than the sea, it is terribly unforgiving of any carelessness, incapacity or neglect.
DTW
YIP
ESA

## Slide 6
DTW
YIP
ESA

## Slide 7
Is something or someone out there trying to hurt or kill you?
Springfield-Branson Airport, June 27, 2018
(click here to play video)
DTW
YIP
ESA

## Slide 8
Is someone or something out there trying to hurt or kill you?
DTW, Runway 22L, February 2, 2016 (open runway incursion video in the path “H:\FAR 139 Training Presentations\FAR 139.303 and 139.329 Airport Movement Area Driver Training\Supporting and unused materials”)
DTW
YIP
ESA

## Slide 9: Training Topics
Topics
  FAR Part 139 Requirements
  Prerequisites to Operate a Vehicle on Movement Areas
    Airport Movement and Non-Movement Areas
    Airport Movement LOAs
    SMGCS (DTW only)
    Runway Protected Areas
    Airfield Markings, Lights, and Signs
    Airfield Radio Communications and Procedures
    Runway Incursion Awareness
    Runway Close/Open Procedures
    Situational Awareness
    Airfield Safety and Runway Incursion Prevention
  Evaluations
    Airfield Safety Exam
    Map Test
DTW
YIP

## Slide 10: Training Topics
Topics
    Prerequisites to Operate a Vehicle on Movement Areas
    Airport Movement and Non-Movement Areas
    Airport Movement LOAs
    SMGCS (DTW only)
    Runway Protected Areas
    Airfield Markings, Lights, and Signs
    Airfield Radio Communications and Procedures
    Runway Incursion Awareness
    Runway Close/Open Procedures
    Situational Awareness
    Airfield Safety and Runway Incursion Prevention
  Airfield Driving Tour/Situational Awareness (initial training only)
ESA

## Slide 11
Breaks
    About 1 per hour for about 10 minutes.
    Please return on time, we have a lot of material to cover!
  Restrooms
    Around the corner past the kitchenette sink.
  Food/drinks
    Feel free to drink/munch during class.
    Food/drinks on the third floor.
  Lunch
    About 45 minutes, depending on progress in class.
  Cell phones
    Please place on ‘vibrate’ or turn them off.
    Do not refer to your cell phones while we are in class.
    You will have plenty of time during breaks and lunch to look at your phones.
    If you have a personal situation where you might have to respond to a text or call you receive while in class, please see me before class starts.
DTW
YIP
ESA
Administrative Notes (classroom only)
CLASSROOM ONLY

## Slide 12
Handouts and what you see on the screen
    Feel free to refer to the handouts and make notes on them.
    Do NOT bury your eyes in the handouts.
    We will NOT “read” the presentation to you.
    We WILL talk about information that’s not always in the presentation, pay attention to the screen and what we’re saying.
  Training – first classroom day
    Lots of presentations and information coming at you.
    If you start to get sleepy/droopy-eyed during class, stand up and stretch as much as you need to while continuing to listen.
    Training – second classroom day
      Classroom communications exercises (written and verbal) – teamwork encouraged!
      Written safety exam (may be deferred to driving days).
      Written map tests (may be deferred to driving days).
DTW
YIP
ESA
Administrative Notes (classroom only)
CLASSROOM ONLY

## Slide 13
Training – airfield driving (normally two days)
    One-on-one driving on the airfield.
    Point-to-point driving exercises.
    Simulated communications with instructor to learn how to communicate with air traffic control.
    Learning the airfield.
    Using lights/signs/markings to safely navigate the airfield.
    Driving evaluation
    See the handout “Movement Area Driver Initial Certification – taxiways/crossing runways (unescorted).
    Your evaluation will be based on the standards in the handout.
    You will do several point-to-point driving exercises and a runways crossing exercise while communicating with an air traffic controller.
  Questions/comments?
DTW
YIP
ESA
Administrative Notes (classroom only)
CLASSROOM ONLY

## Slide 14
FAR Part 139 requires:
§ 139.303 Personnel.
In a manner authorized by the Administrator, each certificate holder must―
(c) Train all personnel who access movement areas and safety areas and perform duties in compliance with the requirements of the Airport Certification Manual and the requirements of this part. This training must be completed prior to the initial performance of such duties and at least once every 12 consecutive calendar months. The curriculum for initial and recurrent training must include at least the following areas:
(1) Airport familiarization, including airport marking, lighting, and signs system.
(2) Procedures for access to, and operation in, movement areas and safety areas, as specified under § 139.329.
(3) Airport communications, including radio communication between the air traffic control tower and personnel, use of the common traffic advisory frequency if there is no air traffic control tower or the tower is not in operation, and procedures for reporting unsafe airport conditions.
DTW
YIP
ESA
FAR Part 139 Requirements

## Slide 15: Prerequisites to Operate a Vehicle on the Airport Movement Area
Airport Authority
DTW 00/00
Doe,
John
a valid and current state-issued driver’s license, not suspended or revoked.
a valid and current airport security badge issued by Airport Security, not suspended or revoked.
a valid reason for entering the movement area (i.e., work-related tasks).
a current training date (no more than 12 consecutive calendar months since date of previous training).
DTW
YIP
ESA

## Slide 16: Airfield Safety
Airport Operations Area (AOA)
            How would you describe the AOA?
            What two areas does the AOA include?
Review DTW YIP
Notes: Everything inside the airport perimeter fence.

## Slide 17: Airfield Safety
Airport Operations Area (AOA)
            Defined as a portion of an airport, specified in the airport security program, in which security measures specified in Title 49 of the Code of Federal Regulations are carried out.
            Generally described as the area within the airport perimeter fence.
            Includes Airport Movement Areas and Non-Movement Areas.
            It is CRITICAL to airfield safety to know the differences between airport Movement and Non-Movement areas.
DTW
YIP
ESA

## Slide 18
Components of Non-Movement Areas
            What are the three components of non-movement areas?
            Who or what controls non-movement areas?
            Is permission required to enter a non-movement area?
            What is the speed limit on zipper roads?
            Which has the right-of-way on non-movement areas – vehicles, or aircraft?
Review DTW YIP
Notes: Ramps/aprons, taxilanes, deice pads.
NMAs are uncontrolled or controlled by a ramp controller.
Permission not required to enter but must meet basic prerequisites for driving on the movement area.

## Slide 19: Airfield Safety
Components of Non-Movement Areas
            Taxilanes – provide routes for aircraft between ramps/aprons
            and movement areas. ONLY found in Non-Movement Areas.
            Ramps (Aprons) – aircraft parking, loading, and servicing.
            De-Ice Pads – for deicing aircraft prior to takeoff.
            Non-movement areas for both airports are shown in
            YELLOW.
19
DTW
YIP
ESA
Initial – DTW & YIP MA maps
Notes: Have trainees pull out the DTW and YIP movement area maps.

## Slide 20: Airfield Safety
Components of Non-Movement Areas
            Aircraft, vehicles, and pedestrians in non-movement areas are NOT controlled by the FAA Air Traffic Control Tower (ATCT).
            All vehicles MUST give way to aircraft at ALL times, unless told otherwise by a controller.
Permission from ATCT to enter non-movement areas is not
required.
Speed limit on zipper roads is 15 MPH.
20
DTW
YIP
ESA
Vehicles should remain on the Zipper Roads unless absolutely necessary to leave them.

## Slide 21
Aircraft Push Back
What four clues tell you that an aircraft is about to push back from a gate?
Review DTW YIP
Notes: Wing walkers – tug connected to aircraft - rotating beacon - absence of support equipment

## Slide 22
Aircraft Push Back
Wing walkers on or near the zipper road.
Tug hooked up to the nose gear and manned.
Absence of support equipment around the aircraft (baggage carts, lav carts, baggage belt carts, etc).
Red rotating beacons flashing (on top and bottom of aircraft).
X
Aircraft pushing back from and taxiing to a gate ALWAYS have the right of way!
How do you know that an aircraft is about to push back from a gate?
X
DTW
ESA

## Slide 23: Airfield Safety
            What are the two areas within the AOA?
            Who or what controls aircraft and vehicles on the movement area?
Airport Movement Area
Components of the AOA
Review DTW YIP

## Slide 24: Airfield Safety
DTW
YIP
ESA
Components of Movement Areas
            Runways – protected areas for aircraft taking off and landing.
            Taxiways – provide routes between Non-Movement Areas and
            runways.
              Taxiways are the same as taxilanes, but are found ONLY in Movement Areas.

## Slide 25: Airfield Safety
All vehicles and pedestrians on the movement areas are controlled by FAA ATCT unless otherwise described in the LOAs (there are exceptions).
Each airport has a Letter of Agreement (LOA) between it and the airport’s FAA ATCT.
The LOAs describe how aircraft, vehicles, and pedestrians on the movement areas will be controlled on the movement areas.
Letters of Agreement
DTW
YIP
ESA
Entering a Movement Area or a Runway without ATCT permission, either on foot or in a vehicle, will result in the person being charged with a
SURFACE INCIDENT or
RUNWAY INCURSION.
Initial – DTW & YIP MA LOAs
Notes: Have trainees pull out the DTW and YIP movement area LOAs

## Slide 26: Airfield Safety
What does “LOA” stand for?
What or who does the LOA affect?
Airport Movement Area
Review DTW YIP
Notes: LOA affects vehicles and aircraft on the movement area.

## Slide 27
DTW & YIP Airport Movement Area LOAs
What five conditions must be met for a person to drive on the movement area without an escort? (four of them have already been discussed).
What is required if a person who does not meet those conditions needs to drive on the movement area?
Review DTW YIP
Notes: - Valid driver’s license - security badge - work-related need - current training - aviation radio
- Must be escorted

## Slide 28
Vehicle operators are required to use the proper phraseology when talking on the radio.
To the extent possible, all vehicles are required to travel to and from work sites via access and zipper roads instead of taxiways and runways.
All vehicles must give way to aircraft unless a controller specifically says that an aircraft will give way.
To the extent possible, conduct runway crossings at the departure end of active runways.
Read back all instructions, ESPECIALLY those involving a runway, or permissions to proceed.
Airport Movement Area - General
DTW
YIP
ESA

## Slide 29
DTW & YIP Airport Movement Area LOAs
You are allowed to drive unescorted on the movement area if you have been trained and certified by Airfield Operations.
  The standards you must meet to be certified are in the driver certification letter in you training packet (initial training only).
  If you have not been trained and certified to drive unescorted, or you don’t have a working aviation radio in your vehicle, you MUST be escorted by someone who has been trained and certified and does have a working radio.
Your vehicle must be equipped with a working aviation radio.
You must listen to the appropriate radio frequency to maintain good situational awareness and identify any possible conflicts with aircraft and other vehicles.
You must always give way to aircraft unless a controller specifically says that an aircraft will give way.
DTW
YIP
ESA
Initial – MA driver cert letter
Notes: Have trainees pull out the AMA driver certification letter

## Slide 30
DTW & YIP Airport Movement Area LOAs
At DTW, you may enter the movement area and drive on taxiways without communicating with ATCT, unless you are escorting another vehicle.
At YIP, you must ALWAYS get ATCT permission to enter the movement area BEFORE entering.
At both airports, if you are trained and certified, you can escort other persons and vehicles on the AMA.
When you escort other vehicles, you must FIRST get ATCT permission to enter the movement area.
  Tell ATCT on first contact that you are escorting other vehicles.
DTW
YIP
ESA

## Slide 31
DTW
DTW & YIP Airport Movement Area LOAs
ARFF vehicle operators on an emergency run
Must give way to all aircraft unless told otherwise by a controller.
Must advise ATCT when clear of the movement area.
Must remain clear of open runways unless authorized by ATCT.
YIP

## Slide 32
Closed surfaces
All vehicle operators may drive on closed runways and taxiways without contacting ATCT to move from one location in the closed area to another.
This includes operators who need to be escorted on the movement area.
  Before leaving a closed area and entering an open area (i.e., a runway or taxiway), persons must be escorted and the escort must first contact ATCT to enter the open area.
When driving on closed surfaces, you MUST give way to ALL aircraft unless an air traffic controller tells you otherwise.
You must still maintain good situational awareness and identify any possible conflicts with aircraft and other vehicles.
  Listen to the correct ground frequency.
  Keep up a good visual scan (both close and distant).
DTW
DTW & YIP Airport Movement Area LOAs
YIP
ESA

## Slide 33
Closed surfaces (continued)
Example: you are northbound on Runway 4R, leading a snow team.
  You are approaching Taxiway V.
  An aircraft is eastbound on Taxiway V approaching 4R.
  You must either:
    1) Give way to the aircraft, or
    2) Contact Ground to ask if the aircraft can give way.
  Be prepared to STOP if the controller tells you that the aircraft CANNOT give way.
DTW
ESA
DTW & YIP Airport Movement Area LOAs

## Slide 34
If the vehicles are slow-moving or unable to give way to aircraft, you must advise ATCT. They may route you differently, or even have you hold your position if there are a lot of aircraft moving on the AMA.
DTW
YIP
DTW & YIP Airport Movement Area LOAs

## Slide 35
SMGCS Plan (DTW)
What does SMGCS stand for?
What is it?
At what visibility level does it go into effect?
Who does it affect?
Who is authorized to enter the movement area when SMGCS is in effect, and why?
Bonus question: what happens if visibility/RVR goes below XXX feet?
Review DTW YIP
Notes: - A low visibility plan for air carrier airports when the visibility (RVR) is less than 1,200 feet.
- Affects aircraft and vehicles.
- Access is limited to ARFF, Ops, Field Maintenance, and FAA Tech Ops.

## Slide 36
SMGCS Plan (DTW)
SMGCS = Surface Movement Guidance and Control System
SMGCS is a low visibility taxi plan is required for any airport which has scheduled air carrier takeoff or landing operations with less than 1,200 feet runway visual range (RVR) visibility conditions.
This plan affects both air crew and vehicle operators.
Reduces potential for runway incursions by improved signage, lighting and markings.
Movement Area access is limited to WCAA ARFF, Ops, Field Maintenance, and FAA Tech Ops.
DTW
ESA
Initial – DTW SMGCS handout
Notes: Have trainees pull out the SMGCS plan handout.

## Slide 37
SMGCS Plan/Driving in Reduced Visibility
What are some safety measures that drivers should take when driving during periods of reduced visibility?
Review DTW YIP
Notes: All lights working – drive slow enough to react – slow down when approaching intersections – monitor the right ATCT frequency – STOP and call for help if you get lost or confused (who do you call?).

## Slide 38
SMGCS Plan/Driving in Reduced Visibility
DTW
YIP
ESA
Vehicle headlights and overhead lights (i.e., beacons or strobes) must be on at all times. If one or both headlights or the beacon or strobe are inoperative, or if any of the brake lights are inoperative, the vehicle cannot be driven on any movement or non-movement areas until they are repaired.
Operate the vehicle with extreme caution and at a speed slow enough to react safely and quickly to the unexpected or sudden appearance of any pedestrians, vehicles, or aircraft.
Drive at a speed slow enough to clearly see when you are approaching intersections. Be prepared to stop at any time for aircraft and vehicles that may appear suddenly and unexpectedly.
Click on the picture to read an article and watch a video that shows how little time you have to react when visibility is reduced.

## Slide 39
SMGCS Plan/Driving in Reduced Visibility
Constantly monitor the appropriate ATCT frequency and maintain a mental picture of where aircraft and other vehicles are operating. Be prepared to change the route of travel to avoid aircraft.
Remember, pilots have extremely limited visibility in their cockpits even in good weather and may not be able to see a vehicle until they are very close to it.
If disoriented and in need of assistance finding a way to a safe location, STOP without crossing a runway hold position.
At DTW, contact the ATCT or Airfield Operations (Ops 1 or 734-942-3685) for assistance.
At YIP, contact the ATCT.
Note: YIP does not have a SMGCS plan (not required by FAA).
DTW
YIP

## Slide 40
SMGCS Plan/Driving in Reduced Visibility
Remember, pilots have extremely limited visibility in their cockpits even in good weather and may not be able to see a vehicle until they are very close to it.
If disoriented and in need of assistance finding a way to a safe location, STOP without crossing a runway hold position. Contact your Manager/Foreman or call Airfield Operations on Ops 1 for assistance.
ESA

## Slide 41: Airfield Safety
DTW
YIP
ESA
Runway Protected Areas
        Runway Safety Areas - RSAs
        Instrument Landing System Critical Areas - ILS
        Runway Protection Zones - RPZs

## Slide 42
Runway Protected Areas
What are the dimensions of a runway safety area?
Who or what controls access to a runway and taxiways within a runway safety area?
Who or what controls access into the part of a runway safety area that is not runway and taxiways?
Review DTW YIP

## Slide 43
500’
1000’
RSA Dimensions
Length: Runway Length + 1000’ beyond each threshold
Width: 500’ centered over runway
RSA outside of the runway – NON-movement area –
access controlled by WCAA
4R
22L
Runway – Movement Area – access controlled by ATCT
Edge
of
RSA
DTW
YIP
ESA
Runway Protected Areas
Initial – DTW YIP LOAs - FAA RSA TSA handout
Notes: Have trainees pull out the following documents: DTW and YIP RSA LOAs – FAA Handout FAQ Runway and Taxiway Safety Areas

## Slide 44
What two things help you identify the edge of a runway safety area?
What one thing helps you identify the end of a runway safety area?
Bonus question: what runway end(s) at DTW do not have localizer antennas?
Bonus question: what runway end(s) at YIP do not have localizer antennas?
Review DTW YIP
Runway Protected Areas
Notes: Signs and markings – localizers – mention the runways at DTW and YIP that don’t have localizers.

## Slide 45
Runway Holding Position Signs and markings are always located at taxiways prior to entering a Runway Safety Area.
22L-4R
4R
22L
At DTW, a Localizer antenna array is located at the end of each RSA except for Runway 21R/3L and the approach ends of Runways 27R and 27L
22L-4R
Edge
of
RSA
4R-22L
4R-22L
At YIP, a Localizer antenna array is located at the end of the RSA for Rwy 5/23 only
22L-4R
22L-4R
DTW
YIP
ESA
Runway Protected Areas

## Slide 46
ATCT only controls movement areas and access to them. You must have clearance from ATCT before crossing runway hold position signs and markings.
ATCT does not give clearance or permission to be in non-movement areas, including the non-movement areas around runways.
WCAA controls access to non-movement areas around runways, so Airfield Operations must give authorization in advance for access to them.
A vehicle or person in a runway’s safety area is treated the same as if it is on the paved surface of the runway.
This means being inside the runway safety area for an open runway
without prior authorization IS A RUNWAY INCURSION
even if there are NO aircraft operating on or near the runway!
Always think of a runway as the paved surface plus the surrounding safety area.
Runway Protected Areas
DTW
YIP
ESA

## Slide 47
Protected areas are imaginary surfaces, but they are made apparent by signs and markings.
Runway Protection Zone-RPZ
ILS Critical Area
Runway Safety Area - RSA
DTW
YIP
ESA
Runway Protected Areas
Initial – FAA kneeboard card
Notes: Have trainees take out FAA kneeboard card – Pilot’s Guide to Airport Signs and Markings

## Slide 48
What protected area does this sign protect?
When can a vehicle go past this sign? (two answers).
What marking is associated with this sign and what does it look like?
Review DTW YIP
Runway Protected Areas
Notes: RSA – permission from ATCT, or verification that runway is closed.

## Slide 49
DO NOT CROSS WITHOUT ATCT PERMISSION UNLESS THE RUNWAY IS VERIFIED CLOSED
Runway Safety Areas (RSAs)
DTW
YIP
ESA
Runway Protected Areas

## Slide 50
When can a vehicle go past this sign? (two answers).
What marking is associated with this sign? What does it look like?
Review DTW YIP
Runway Protected Areas
Notes: RSA – permission from ATCT, or verification that runway is closed.

## Slide 51
DTW
YIP
ESA
Runway Protected Areas
DO NOT CROSS WITHOUT ATCT PERMISSION UNLESS THE RUNWAY IS VERIFIED CLOSED
Instrument Landing System (ILS) Critical Areas

## Slide 52
Why is it important to not go into an ILS critical area unless authorized?
How can a vehicle operator determine whether the ILS is operating and in use by an aircraft?
What has to be done if a vehicle or equipment will be remaining in an ILS critical area after the runway is reopened?
Review DTW YIP
Runway Protected Areas
Notes: Interference with signals – can’t determine, must always obtain permission from Ground to enter – contact Ground

## Slide 53
Vehicles, aircraft, equipment, or other objects in an ILS critical area could interfere with an ILS signal and pose a safety hazard to aircraft using the ILS.
Aircraft can use ILS signals to land at any time, regardless of weather conditions. Good weather is NOT an indication that an ILS is not being used.
Vehicle operators have no way of knowing when an aircraft is using an ILS.
All vehicle operators must contact Ground for clearance into and/or through an ILS critical area, unless the runway is closed.
When a runway is being reopened, if any vehicles will be remaining in an ILS critical area, Ground must be notified.
At least 24-hour notice must be given to FAA Tech Ops before conducting mowing operations around ILS localizer antennas.
DTW
YIP
ESA
Runway Protected Areas

## Slide 54
Vehicles, aircraft, equipment, or other objects in an ILS critical area could interfere with an ILS signal and pose a safety hazard to aircraft using the ILS.
Aircraft can use ILS signals to land at any time, regardless of weather conditions. Good weather is NOT an indication that an ILS is not being used.
Vehicle operators have no way of knowing when an aircraft is using an ILS.
All vehicle operators must contact Ground for clearance into and/or through an ILS critical area, unless the runway is closed.
Runway Protected Areas

## Slide 55
You are being directed by ATCT to take a specific route that requires you to go through an ILS critical area before crossing a runway. The controller will tell you to do one of three things before arriving at the ILS hold position. What are they?
Review DTW YIP
Runway Protected Areas
Notes: Hold short of the critical area – hold short of the runway (implies that you can pass through the critical area to the runway) – cross the runway (implies that you can pass through the critical area to the runway?)

## Slide 56
What type of protected area does this sign protect?
Where is this sign located?
When can a vehicle go past this sign at DTW?
What marking is associated with this sign? What does it look like?
Review DTW YIP
Runway Protected Areas
Notes: DTW – any time (must stay on pavement)
YIP – only with ATCT permission

## Slide 57
DTW
ESA
Runway Protected Areas
This is the ONLY type of red-face sign at DTW that you may pass without ATCT permission,
as long as you do not enter any other protected areas.
Runway Protection Zone

## Slide 58
RPZ: Do not penetrate this imaginary surface without ATCT clearance
A Runway Protected Zone (RPZ) is an area off the runway end used to help protect people and property under the approach to the runway. The RPZ is trapezoidal in shape and centered on the extended runway centerline.
The approach above the RPZ is protected by an imaginary surface. The surface starts at ground level 200 feet from the threshold of the runway and slopes up and away from the runway.
The surface cannot be penetrated by aircraft, vehicles, or other objects without ATCT permission.
However, aircraft, vehicles, or other objects that are short enough to pass below the imaginary surface may do so without ATCT permission, as long as they do not enter any other protected areas (for example, RSAs) without permission.
DTW
ESA
Runway Protected Areas

## Slide 59
RPZ - Taxiway K @ 22L Approach
Remain on pavement when passing the signs to pass under the imaginary surface.
Imaginary surface
DTW
ESA
Runway Protected Areas
Rwy 4R – 22L

## Slide 60: Overview of Runway Safety Areas (RSAs) and ILS Critical Areas at DTW
Runway Safety Areas
ILS Critical Areas
DTW
ESA

## Slide 61
ILS Critical Areas and RSAs at YIP
YIP
Runway Safety Areas
ILS Critical Areas
ESA

## Slide 62
Airfield Markings, Lights, and Signs
§ 139.303 Personnel.
In a manner authorized by the Administrator, each certificate holder must―
(c) Train all personnel who access movement areas and safety areas and perform duties in compliance with the requirements of the Airport Certification Manual and the requirements of this part. This training must be completed prior to the initial performance of such duties and at least once every 12 consecutive calendar months. The curriculum for initial and recurrent training must include at least the following areas:
(1) Airport familiarization, including airport marking, lighting, and signs system.
DTW
YIP
ESA

## Slide 63
Airfield Markings
Zipper roads are located on non-movement areas next to terminals.
At DTW, some zipper roads cross taxilanes between terminals.
Vehicles on a zipper road must give way to:
ALL aircraft that are crossing or about to cross a zipper road, include aircraft that are pushing back from a gate.
ALL vehicles that are on a taxilane and crossing or about to cross a zipper road.
Vehicle access (zipper) road
NO EXCEPTIONS!
DTW
YIP
ESA

## Slide 64
Airfield Markings
Runway Holding Position
What does a runway hold position marking look like?
Which side of the marking do you hold on?
One of two things is required to cross the marking. What are they?
Review DTW YIP
Notes: Permission from ATCT or verification that the runway is closed.

## Slide 65
Airfield Markings
Runway Holding Position
Identifies the position at which pilots and vehicle operators must hold short of a runway safety area or other protected area.
You must at the holding position until given permission to cross by ATCT!
Hold Short on This Side
Which side do you hold short of?
DTW
YIP
ESA
Notes: Have trainees refer to FAA kneeboard card – Pilot’s guide to Airport Signs and Markings

## Slide 66
Airfield Markings
What does a non-movement area boundary marking look like?
Which side of the marking do you hold on?
At DTW, when is it permissible to cross the marking without ATCT permission?
At YIP, when is it permissible to cross the marking without ATCT permission?
Non-Movement Area Boundary
Review DTW YIP
Notes: - DTW - vehicle operator is authorized and trained to drive unescorted on the movement area and has a functioning aviation radio, AND is not escorting another vehicle. OR the surface past the marking is verified CLOSED.
- YIP – only when the surface past the marking is verified CLOSED.

## Slide 67
Airfield Markings
Non-Movement Area Boundary
Marks the boundary between movement and non-movement areas.
Authorized WCAA/FAA vehicle operators at DTW may access movement areas (except for open runways) by monitoring the appropriate ground control frequency.
Vehicle operators who are escorting other vehicles must contact ATCT before entering the movement area.
Vehicles operating at YIP must contact ATCT before entering the movement area.
Which side is the non-movement side?
Non-movement side
DTW
YIP
ESA

## Slide 68
Airfield Markings
ILS Critical Area Marking
What does an ILS critical area marking look like?
Which side of the marking do you hold on?
One of two things is required to cross the marking. What are they?
Review DTW YIP
Notes: Permission from ATCT or verification that the runway is closed.

## Slide 69
Airfield Markings
ILS Critical Area Holding Position
Protects the area through which ILS signals are transmitted.
Vehicles and aircraft in the ILS critical area can interfere with the signals.
Do not cross this marking without permission from ATCT, unless the runway is closed.
DTW
YIP
ESA

## Slide 70
Airfield Markings
Taxiway Edge Marking
There are two types of taxiway edge markings. What do they look like?
One type is placed between pavement usable by aircraft and pavement NOT usable by aircraft. Which type is it?
Review DTW YIP
Notes: Permission from ATCT or verification that the runway is closed.

## Slide 71
Airfield Markings
Continuous Taxiway Edge
Dashed Taxiway Edge
Alt. Dashed Taxiway Edge
Taxiway Edge Marking
Two types of lines – continuous, and dashed.
Aircraft - yes
Aircraft - no
Aircraft – OK both sides
No useable pavement for aircraft on the other side of the line.
Dashed - aircraft can use pavement on both sides of the line.
DTW
YIP
ESA

## Slide 72
Airfield Markings
Oops!
Taxiway Edge Marking
Photo on Airliners.net by SkyArts Aviation Photography
DTW
YIP
ESA

## Slide 73
Airfield Markings
What marking is this?
What is it used for?
Review DTW YIP
Notes: Taxiway hold position – shows where to stop for adequate space for aircraft to go by.

## Slide 74
Airfield Markings
Taxiway Holding Position
Can be seen approaching a taxiway intersection where ATCT normally holds aircraft short of a taxiway intersection.
Allows adequate wingtip clearance for aircraft passing through the intersection.
Do not confuse this marking with movement/non-movement area boundary markings OR dashed taxiway edge lines.
DTW
ESA

## Slide 75
Airfield Markings
Taxiway Centerline
Are vehicle operators required to follow this line when driving on a taxiway or taxilane?
Bonus question: are aircraft required to follow this line when taxiing?
Review DTW YIP
Notes: No to both (example for aircraft – oversteering)

## Slide 76
Airfield Markings
Taxiway Centerline
Provides pilots a visual cue to permit taxiing along a designated path.
DTW
YIP
ESA

## Slide 77
Airfield Markings
What does an enhanced taxiway centerline look like?
Where is it found?
Why can it be valuable to a vehicle operator?
Bonus question – how long is it?
Review DTW YIP

## Slide 78
Airfield Markings
Enhanced Taxiway Centerline
Gives warning that a runway hold short position marking is located ahead. Especially helpful during conditions of reduced visibility.
Be prepared to at the runway hold short position until cleared onto or across the runway by ATCT.
DTW
YIP
ESA

## Slide 79
Airfield Markings
Geographic Position Marking (“Spots”)
What spot numbers are found at the north and south ends of the McNamara Terminal?
What spot numbers are found on the Runway 22L deice pad?
What spot numbers are found on Taxilane E next to the North Terminal?
Review DTW YIP

## Slide 80
Airfield Markings
Geographic Position Marking (“Spots”)
Spots are “shorthand” for giving locations on selected taxilanes.
Two spots near the 22L deice pad.
Four spots parallel to and west of the North Terminal (Taxilane E).
Two spots on taxilanes at the north end of the North Terminal (Taxilanes E-7 and E-8).
Four spots on taxilanes at the south end of the McNamara Terminals (J-7, J-8, U-9, Q).
Four spots on taxilanes at the north end of the McNamara Terminals (U-7, U-8, U-9, Q).
Each spot at the North Terminal is a black number on yellow background.
Each spot at the McNamara Terminal is a yellow number & letter in an open circle.
DTW
ESA

## Slide 81
Airfield Markings
Geographic Position Marking
Spots are “shorthand” for giving locations on selected taxilanes.
Always placed with a non-movement area boundary marking
or taxiway hold position marking.
DTW
ESA

## Slide 82
Airfield Markings
Geographic Position Marking
McNamara Terminal
22L Pad and
North Terminal
Spots 1-8
Spots 1N-4N
Spots 1S-4S
DTW
ESA

## Slide 83
Airfield Markings
Geographic Position Marking
22L pad and North Terminal spots (see DTW movement area map).
Single-digit numbers, numbered south to north.
North Terminal
22L Deice Pad
DTW
ESA

## Slide 84
Airfield Markings
Geographic Position Marking
McNamara Terminal spots – north end (see DTW movement area map)
Combination of a number and letter, numbered east to west.
1N
2N
3N
4N
Taxilane Q
Taxilane U-9
Taxilane U-8
Taxilane U-7
DTW
ESA

## Slide 85
Airfield Markings
Geographic Position Marking
McNamara Terminal spots – south end (see DTW movement area map)
1S
2S
3S
4S
Taxilane J-7
Taxilane J-8
Taxilane U-9
Taxilane Q
DTW
ESA

## Slide 86
Airfield Markings
Runway Markings
What color are runway markings?
What should you do if you see white pavement markings and have not received permission from ATCT to be there?
Review DTW YIP
Notes: Get off the runway ASAP and call ATCT or Airfield Operations

## Slide 87
Runway Markings
Runway markings come in a variety of sizes and shapes. They are all WHITE. If you are seeing white markings, you are on the Movement Area and have ENTERED A RUNWAY. If the runway is OPEN and you did NOT receive permission from ATCT to be on the runway, EXIT IMMEDIATELY, call ATCT or Airfield Operations, and tell them where you are!
DTW
YIP
ESA
Airfield Markings

## Slide 88
No vehicles, equipment, or pedestrians on these markings when aircraft of ANY size are in the yellow “box” on Twy M. Drive AROUND the markings.




DTW
ESA
Vehicle Restriction on Twy M Access Road
Airfield Markings

## Slide 89
The restriction applies to a 450-foot long section of the access road next to the south end of Taxiway M.
The area on the road marked with white lines is in the Taxiway Object Free Area (TOFA) for Taxiway M.
DTW
ESA
Airfield Markings
Vehicle Restriction on Twy M Access Road

## Slide 90
Runway Holding Position
ILS Critical Area
Holding Position
Continuous Taxiway Edge
Dashed Taxiway Edge
Dashed Taxiway Edge
Taxiway Centerline
Taxiway Holding Position
Movement/Non-Movement
Area Boundary
Enhanced Taxiway Centerline
DTW
YIP
ESA
Airfield Markings
Initial – FAA kneeboard card

## Slide 91
Airfield Lighting
What is this light?
Where is it found besides on taxiways?
Bonus question: as long as you are on pavement that has these lights, you can be certain that you are not in a runway protected area. True or false? Why?
Review DTW YIP

## Slide 92
Taxiway edge lights identify the edge of the usable taxiway or taxilane surface at night and during periods of low visibility.
Taxiway edge lighting is blue.
Taxiway Edge Lighting
Airfield Lighting
DTW
YIP
ESA

## Slide 93
Airfield Lighting
What are these lights?
Bonus question: these lights are found on both movement and non-movement areas. True or false?
Bonus question #2: these lights can be found on a runway at DTW. True or False? If true, what runway?
Review DTW YIP

## Slide 94
Taxiway Centerline Lighting
Taxiway centerline lights are green.
They are placed on selected taxiways and taxilanes to assist pilots with taxiing at night and during periods of reduced visibility.
They are also placed on Rwy 9L/27R between 4R/22L and 3L/21R, since that section of runway is normally used as a taxiway.
Airfield Lighting
DTW
ESA

## Slide 95
Airfield Lighting
What are these lights?
Where are the amber and white lights found?
Review DTW YIP

## Slide 96
Runway edge lights Identify the edge of the usable runway surface at night and during periods of low visibility.
Runway edge lights are clear (or white), except for the last 2000’ of a precision or non-precision instrument runway. The half of the lights facing the pilot are amber.
Airfield Lighting
Runway Edge Lights
DTW
YIP
ESA

## Slide 97
Airfield Lighting
What color or colors are runway centerline lights?
Where (i.e., what distance(s) would you find the red lights at?
Runway Centerline Lights
Review DTW YIP

## Slide 98
Runway Centerline Lighting
Airfield Lighting
Runway centerline lights give pilots a visual reference for the centerline.
They are clear (or white), except for the last 3000’ of a precision or non-precision instrument runway.
Starting at 3000’ remaining, the lights are alternating red and white.
Starting at 1000’ remaining, the lights are all red.
DTW
YIP
ESA

## Slide 99
Airfield Lighting
What are these lights?
Where are they found?
Review DTW YIP

## Slide 100
Elevated Runway Guard Lights (wig-wags)
Used to identify the holding position for a runway especially at night and during periods of low visibility.
Elevated runway guard lights are amber.
DTW
YIP
ESA
Airfield Lighting

## Slide 101
Airfield Lighting
What are these lights? (They are yellow and flashing).
Where are they found?
Review DTW YIP

## Slide 102
In-pavement runway guard lights are co-located with runway hold bars, above-ground runway guard lights, and hold position signs. These lights are yellow.
At this time, these lights are only installed at certain taxiway intersections at DTW.
DTW
YIP
ESA
Airfield Lighting
In-Pavement Runway Guard Lights (wig-wags)

## Slide 103
Elevated
In-Pavement
DTW
YIP
ESA
In-Pavement and Elevated Runway Guard Lights
Airfield Lighting

## Slide 104
Airfield Lighting
What are these lights called? (They are red and steady-burning when turned “ON”).
What do they tell you when they are on?
Is it safe to pass over the runway hold short position when they are off?
The lights are on, and a controller gives you permission to cross the runway. What should you do?
Review DTW YIP

## Slide 105
Runway Status Light System (RWSL) – DTW ONLY
Designed to reduce the number of runway incursions without interfering with normal and safe airport operations
Automatic system that gives an added layer of safety for the runway environment
Gives warning of a potential conflict on a runway between aircraft and other aircraft and/or vehicles
Indicates runway status only
Provides visual signal to pilots and vehicle operators that it is unsafe to enter, cross, or begin takeoff on a runway.
Does not give or imply clearance
to cross a runway
DTW
ESA
Airfield Lighting
Initial – FAA RWSL handout
Notes: Have trainees pull out FAA handout – Runway Status Lights at DTW

## Slide 106
Stop at the runway hold short position whenever the RELs are “on.”
The lights may cycle on and off while you are waiting for ATCT clearance to cross the runway.
DO NOT PROCEED after the lights go out until ATCT specifically tells you to.
Runway Status Light System (RWSL)
Runway Entrance Lights (RELs)
DTW
ESA
Airfield Lighting

## Slide 107
Provides visual signal to vehicle operators that it is unsafe to enter or cross, a runway.
Stop at the runway hold short position whenever the RELs are “on.”
The lights may cycle on and off while you are waiting for ATCT clearance to cross the runway.
DO NOT PROCEED after the lights go out until ATCT specifically tells you to.
Runway Status Light System (RWSL)
Runway Entrance Lights (RELs)
DTW
ESA
Airfield Lighting

## Slide 108
If ATCT tells you to proceed and the lights are “on”,
DO NOT PROCEED – HOLD YOUR POSITION.
Call ATCT and tell them “[call sign] is holding short of Runway XX at Taxiway X due to red lights.”
If ATCT tells you to proceed and the lights come on after you cross the hold short position,
CLEAR THE RUNWAY IMMEDIATELY AND CALL ATCT
Runway Status Light System (RWSL)
Runway Entrance Lights (RELs)
DTW
ESA
Airfield Lighting

## Slide 109
THLs tell pilots to STOP because of a potential conflict further down the runway.
Vehicles (ARFF or Ops) chasing a landing aircraft may cause the THLs to come on.
No action is required by vehicle operators.
Runway Status Light System (RWSL)
Takeoff Hold Lights (THLs)
DTW
ESA
Airfield Lighting

## Slide 110
Runway Status Light System (RWSL) – DTW ONLY
Show RWSL Video (separate file)
DTW
ESA
Airfield Lighting

## Slide 111
Runway Status Light System (RWSL)
Runway Entrance Lights (RELs) – across runways
Takeoff Hold Lights (THLs) – Runway Thresholds (22L & 21R)
DTW
ESA
Airfield Lighting

## Slide 112
Airfield Lighting
What are these lights? (They are red and steady-burning, not flashing).
Where are they located? (four locations).
Bonus question: One set is turned on only when one certain runway is open. What runway is that, and what taxiway are they located on?
Review DTW YIP

## Slide 113
Vehicle operators must hold short of red illuminated stop bars at the Rwy 27R intersections of 22L and 21R until permission to cross them is received from ATCT.
27R
22L
Runway Stop Bar Lights
22L
27R
21R
One set is located just east of 22L.
A third set of stop bar lights is located on the south side of Rwy 27R, on Twy B. This set is only active when Rwy 27R is open.
Two sets are on each side of 21R.
DTW
ESA
Airfield Lighting

## Slide 114
Airfield Lighting
What is the name of this light and where is it located?
Why is half of it red and half of it green?
Review DTW YIP

## Slide 115
Used to mark the end of useable runway pavement for aircraft.
Lights are split into two colors:
Red face towards the runway
Green face away from runway
Arranged in two sets of four lights.
Runway Threshold Lights
DTW
YIP
ESA
Airfield Lighting

## Slide 116
What is this sign called?
Airfield Signs
What is this sign called?
Review DTW YIP

## Slide 117
Identifies the taxiway on which the aircraft or vehicle is located.
The letters are yellow with a black background.
Taxiway Location Sign
Airfield Signs
DTW
YIP
ESA
Initial – FAA kneeboard card
Notes: Have trainees refer to FAA kneeboard card – Pilot’s Guide to Airport Signs and Markings

## Slide 118
Taxiway Directional Sign
Identifies the direction(s) in which a taxiway goes.
The letters are black with a yellow background.
Taxiway location and directional signs are often co-located together in a sign array.
DTW
YIP
ESA
Airfield Signs

## Slide 119
Arrows on yellow signs point in the direction of a turn ahead
Taxiway/Taxilane Direction and Location Signs
Black sign indicates the taxiway/taxilane that you are on
DTW
YIP
ESA
Airfield Signs

## Slide 120
Taxiway Sign Arrays
Taxiway directional and location signs are often located together at intersections.
Where is this sign located, and in what direction does it face?
DTW
YIP
ESA
Airfield Signs

## Slide 121
Surface Painted Signs
Signs can also be painted on the pavement
Surface Painted Runway
Holding Position
Surface Painted
Taxiway Directional
Surface Painted
Taxiway Location
Airfield Signs
DTW
YIP
ESA

## Slide 122
1
2
3
4
5
1
2
4
3
5
Mandatory Hold Position Sign
Elevated Runway Guard Lights
Surface Painted Hold Position Sign
Runway Holding Position Bar
Enhanced Taxiway Centerline
What are the 7 indications that you’re approaching a runway hold position? (some are not at all intersections)
Airfield Lighting, Marking and Signs
6
6
In-Pavement Runway
Guard Lights
(DTW only, not all intersections)
7
Runway Status Lights
(DTW only, not all intersections)
7
DTW
YIP
ESA

## Slide 123
Airfield Lighting, Marking and Signs
What is missing in this picture?
No lights, signs, or markings to tell you the edge of a runway safety area goes through the concrete island on the left of Taxiway Y.
Taxiway Y edge marking
DTW
ESA

## Slide 124
Airfield Lighting, Marking and Signs
Beware of the “seas of concrete” next to runways
9L-27R
4R-22L
3L-21R
RSA
RSA
No lights, signs or markings are readily visible on the “seas of concrete” to show the edge of the RSA between the runways and Taxiway Y or M
M
Y
DTW
ESA

## Slide 125: Airfield Radio Communications and Procedures
DTW
YIP
ESA
Initial – Communicating at DTW & YIP
Notes: Have trainees pull out WCAA Ops training document – Communicating with ATC at DTW and YIP

## Slide 126
Always use standard FAA ATCT phraseology
Know what you are going to say before you say it
Listen to radio traffic before transmitting.
Do not interrupt other radio transmissions
Listen closely to all instructions
Never make assumptions. If you are not sure of your instructions, then ask ATCT to say it again
Read back all instructions, especially Hold Short instructions and other runway instructions
Always monitor ground control while in the movement area
Make sure equipment is working properly before entering the movement area
DTW
YIP
Radio Communications

## Slide 127
How can listening to the aviation (“FAA”) radio help me?
SITUATIONAL AWARENESS
  Lets you hear where aircraft are and where they’re going.
  Helps you form a “mental map” of what’s going on.
What am I listening for?
  Pilots/vehicle operators giving their location and requesting instructions to go somewhere.
  Controllers telling pilots/vehicle operators what route or routes to take.
  Potential conflicts between you and aircraft/vehicles.
DTW
YIP
ESA
Radio Communications

## Slide 128
Roger- I have received all of your transmission.
      Not to be used to answer “Yes” to a question.
Wilco – I have received your transmission and I will comply.
Affirmative - Yes
Negative - No
Acknowledge – Confirm that you have received my message.
Read back - Repeat message.
Say Again – Request a repeat of instructions.
Stand By - Wait, controller is busy with other tasks. May require waiting several minutes.
DTW
YIP
ESA
Radio Communications

## Slide 129
Go Ahead - State your request.
Proceed - Authorization to begin/continue driving
Advise intentions - What do you plan to do.
Without Delay - Proceed with approved instructions immediately.
Expedite – Comply promptly with instruction.
Immediately – NOW!
Unable – Indicates inability to comply.
Hold - Stay in place, do not move.
Hold Short – Hold short of a specific point as instructed by the controller. Often at Runway/Taxiway intersections
DTW
YIP
ESA
Radio Communications

## Slide 130: Phonetics
A - Alfa
B - Bravo
C - Charlie
D - Delta
E - Echo
F - Foxtrot
G - Golf
H - Hotel
I - India
J - Juliet
K - Kilo
L - Lima
M - Mike
N - November
O - Oscar
P - Papa
Q - Quebec
R - Romeo
S - Sierra
T - Tango
U - Uniform
V - Victor
W - Whiskey
X - X-ray
Y - Yankee
Z - Zulu
0 - Zee-ro
1 - Wun
2 - Too
3 - Tree
4 - Fow-er
5 - Fife
6 - Six
7 - Sev-en
8 - Ait
9 - Niner
Letters
Numbers
DTW
YIP
ESA
Radio Communications

## Slide 131
What is a Read Back?
  Repeating an ATCT instruction verbatim.
You will hear pilots and drivers reading back instructions.
Readbacks give you a second chance to hear a controller’s instructions and help you maintain “situational awareness.”
You are required to read back ALL runway instructions, especially HOLD SHORT instructions.
Also Read Back instructions:
  To drive requested routes.
  To change frequencies.
  That are changes to previous Instructions.
DTW
YIP
Radio Communications

## Slide 132
What is a Read Back?
  Repeating an ATCT instruction verbatim.
You will hear pilots and drivers reading back instructions.
Readbacks give you a second chance to hear a controller’s instructions and help you maintain “situational awareness.”
ESA
Radio Communications

## Slide 133: Radio Communications
In proper order, what do ATCT controllers expect to hear when you make initial contact with them?
Review DTW YIP

## Slide 134
What do ATCT controllers expect to hear when you make initial contact with them?
Who you are calling
Who you are
Where you are (your location)
Where are you going
And only if applicable:
What will you be doing when you get there, and for how long
DTW
YIP
Radio Communications

## Slide 135
What do ATCT controllers expect to hear?
Who the pilot/driver is calling
Who the pilot/driver is (their call sign)
Where they are (their location)
Where they want to go
And only if applicable:
What they will be doing when they get there, and for how long
ESA
Radio Communications

## Slide 136
Who you are calling: “XXXXX Ground” or “XXXXX Tower”
Who you are: “your call sign.”
  PAUSE: wait for acknowledgement from ATCT:
  XXXXX Ground “(or XXXXX Tower)”
Repeat your identification number, and say where you are: “your call sign” is at [location].”
Where you are going: “Would like to go to [location].”
  - ATCT response: “your call sign, [gives instructions].”
Your response: “your call sign [read back instructions word for word].”
Follow the instructions.
DTW
YIP
ESA
Radio Communications

## Slide 137
Example (point to point on taxiways):
(you) “Metro Ground, Ops 39”
(pause, wait for response)
(ATCT) “Ops 39, Metro Ground.”
(you) ”Ops 39 is on Taxiway Kilo at Kilo-7, would like to go to Mike at Mike-5.”
(ATCT) “Ops 39, proceed via Kilo, Victor, Mike.”
(you) “Ops 39 proceeding via Kilo, Victor, Mike.”
DTW
Radio Communications

## Slide 138
Example (point to point on taxiways, crossing a runway):
(you) “Metro Ground, Ops 39”
(pause, wait for response)
(ATCT) “Ops 39, Metro Ground.”
(you) “Ops 39 is on Taxiway Tango at Tango-3, would like to go to Kilo at Kilo-4.”
(ATCT) “Ops 39 proceed via Taxiway Tango, hold short Runway 21L.”
(you) “Ops 39 proceeding via Tango, holding short Runway 21L.”
(you) Follow directions – when you reach the hold position on Tango at Runway 21L, stop and WAIT.
DTW
Radio Communications

## Slide 139
Example (point to point on taxiways, crossing a runway continued):
When ATCT is ready to have you cross the runway:
(ATCT) “Ops 39, cross Runway 21L, continue via Tango, Kilo.”
(you) ”Ops 39 crossing Runway 21L, continue via Tango, Kilo.”
(you, after you finish crossing) “Ops 39 is clear of Runway 21L.”
(ATCT) “Ops 39, Roger.”
DTW
Radio Communications

## Slide 140
Example (crossing a runway):
(you) “Metro Ground, Ops 39”
(pause, wait for response)
(ATCT) “Ops 39, Metro Ground.”
(you) “Ops 39 is on Taxiway Tango, holding short of Runway 21L, would like to cross 21L.”
ATCT will tell you at this point to either “HOLD SHORT”, or “CROSS”. If they tell you to “HOLD SHORT”:
(ATCT) “Ops 39, hold short Runway 21L.”
(you) “Ops 39, holding short Runway 21L.”
DTW
Radio Communications

## Slide 141
Example (crossing a runway, continued):
When ATCT is ready to have you cross the runway:
(ATCT) “Ops 39, cross Runway 21L.”
(you) ”Ops 39 cross Runway 21L.”
(you, after you finish crossing) “Ops 39 is clear of Runway 21L.”
(ATCT) “Ops 39, Roger.”
DTW
Radio Communications

## Slide 142
Example (point to point on taxiways):
(you) “Willow Ground, Ops 39”
(pause, wait for response)
(ATCT) “Ops 39, Willow Ground.”
(you) ”Ops 39 is on the East Ramp at Taxiway Echo-2, would like to go to the South Ramp.”
(ATCT) “Ops 39, proceed via Echo-2, Hotel, Delta.”
(you) “Ops 39 proceeding via Echo-2, Hotel, Delta.”
(you) “Ops 39 clear of Delta.
(ATCT) “Ops 39, roger.
YIP
Radio Communications

## Slide 143
Example (point to point on taxiways, crossing runways):
(you) “Willow Ground, Ops 39”
(pause, wait for response)
(ATCT) “Ops 39, Willow Ground.”
(you) “Ops 39 is on the East Ramp at Taxiway Golf, would like to go to the West Ramp.”
(ATCT) “Ops 39 proceed via Taxiway Golf, hold short Runway 23.”
(you) “Ops 39 proceeding via Golf, holding short Runway 23.”
(you) Follow directions – when you reach the hold position on Golf at Runway 23, stop and WAIT.
YIP
Radio Communications

## Slide 144
Example (point to point on taxiways, crossing runways continued):
When ATCT is ready to have you cross the runway:
(ATCT) “Ops 39, cross Runway 23L, proceed via Golf.”
(you) ”Ops 39 crossing Runway 23, proceeding via Golf.”
(you, after you finish crossing) “Ops 39 is clear of Runway 23.”
(ATCT) “Ops 39, Roger.”
YIP
Radio Communications

## Slide 145
DTW
YIP
  Additional notes
  Follow the instructions.
    Listen to and follow what the controller actually says and not what you THINK they will say.
    It’s easy to have a route in mind and then get confused when the controller gives you a route you didn’t expect.
    If you are unsure about what the controller said, ask for a repeat (“Say again for Ops 39”).
    When doing a readback, read back exactly what the controller said.
      Don’t add any extra words or embellishments such as “would like permission to…” or “requesting clearance”.
      You don’t need to say “roger”, your verbatim readback is enough.
Radio Communications

## Slide 146
DTW
YIP
  Additional notes (continued)
    Always include your call sign in a transmission.
      That tells the controller that the correct person is responding.
    Be patient.
      The controller may be busy with a briefing, position change, or handoff with another controller, or they may be working multiple frequencies.
      If it becomes evident that the controller didn’t hear you, simply call them again as described above and wait for them to reply.
Radio Communications

## Slide 147
IMPORTANT: if you need permission to enter or drive on the movement area, do not proceed without ATCT instructions (unless it is an emergency).
If you cannot contact a controller after repeated attempts:
  Lack of response from ATCT does not imply permission to proceed.
  Contact Airfield Operations Dispatch on a county radio (tune to channel Ops 1, call “Station 3”) and ask for assistance in contacting ATCT.
  Station 3 will contact ATCT to have a controller make contact.
If you cannot communicate with ATCT because of a faulty aviation radio, leave the movement area without interfering with aircraft movements and ask Station 3 to advise ATCT.
DTW
YIP
Radio Communications

## Slide 148
If it is an emergency:
  Reposition as necessary to avoid aircraft and prevent injury and damage to property.
  Immediately contact Airfield Operations to relay details to ATCT, and stand by for further instructions.
  Do not cross an open runway or enter a runway safety area when repositioning.
DTW
YIP
Radio Communications

## Slide 149
Review Written Exercises (DTW) (initial training only)
Point-to-Point (1-4)
Communications/Navigation Exercises (1-6)
DTW
Radio Communications
Initial – P to P and Comm/Nav exercises
Notes: Have the trainees pull out the Point-to-Point and Comm/Nav exercises

## Slide 150
Multiple Runway Crossings
An FAA notice in June 2010 stated that:
    An explicit runway crossing clearance must be issued for every runway crossing (whether runway is open or closed)
    A vehicle must have crossed the previous runway before another runway crossing clearance is issued
DTW
YIP
Radio Communications

## Slide 151: Radio Communications
What controller do you talk to when driving taxiways and crossing open runways?
What controller do you talk to when driving open runways?
On Midnight shift (DTW only), after all runways but one have been closed, how do you find out what frequency the controller will be operating on? (Frequencies combined into one).
Review DTW YIP

## Slide 152
Ground Controller: drive on taxiways and cross open runways.
Tower (local) Controller: drive on open runways.
DTW
  Frequencies are combined during slow periods.
  Midnight shift frequencies combine to one Tower frequency, check ATIS
  Frequencies in RED are the DTW Ground frequencies you should normally use
 | Tower | Ground | ATIS | X-Wind
DTW | 135.0 (W) 118.4 (E) | 121.8 (NW) 119.45 (NE) 119.25 (SE) 132.725 (SW) | 133.675 (Arr) 118.125 (Dep) | 128.75
YIP | 125.275 | 119.975 | 127.425 | N/A
DTW
YIP
ESA
Radio Communications

## Slide 153
Frequencies you should monitor:
  121.8 (North)West Ground
  119.45 (North) East Ground
  133.675 ATIS Arrivals- Automated Terminal Information System
ESA
Radio Communications

## Slide 154
  What are the two Tower (local) frequencies and what part of the airfield does each cover?
  What are the four Ground frequencies and what part of the airfield does each cover?
  Which west-side Ground frequency is used when only one controller is working that side of the field (i.e., combined frequencies)?
  Which east-side Ground frequency is used when only one controller is working that side of the field (i.e., combined frequencies)?
  Bonus question: what are the two ATIS frequencies?
Radio Communications
Review DTW only
Notes: 133.675 ATIS Arrivals
118.125 ATIS Departures

## Slide 155
DTW Tower and Ground Control Frequencies
West Tower 135.0
SW Ground
132.72
East Tower 118.4
SE Ground
119.25
NE Ground
119.45
NW Ground
121.8
DTW
Initial – DTW ATCT Frequencies handout
Notes: Have trainees pull out the Airport Diagram – DTW Tower and Ground Control Frequencies

## Slide 156
DTW Ground Control Frequencies
SW Ground
132.72
SE Ground
119.25
NE Ground
119.45
NW Ground
121.8
ESA
Initial – DTW ATCT Frequencies handout

## Slide 157
Radio Communications
COLOR AND TYPE OF SIGNAL
Steady Green
Steady Red
Flashing Red
Alternating
Flashing White
Review DTW YIP

## Slide 158
COLOR AND TYPE OF SIGNAL
Steady Green
Steady Red
Flashing Red
Alternating
Flashing White
MEANING for VEHICLES
Cleared to cross, proceed or go
Stop
Clear the taxiway or runway
Exercise extreme caution
Return to starting point on airport
DTW
YIP
ESA
Radio Communications
Initial – FAA Kneeboard card

## Slide 159
What should you do if your aviation radio stops working while you are driving on the movement area?
When is it permissible to continue driving and working on the movement area without a working aviation radio?
When can a cell phone be used to communicate on the movement area?
The edge lights for the surface you’re on are flashing. What does that mean, and what should you do?
Radio Communications (DTW)
Review DTW only
Notes: Get clear and remain clear of the movement area.
Only when escorted by another vehicle with a working aviation radio and driven by a trained airfield driver.
Only in an emergency, when there is no other way to communicate with Tower or Airfield Operations
ATCT is trying to contact you.

## Slide 160
Loss of Radio Communications
Immediately get clear of movement areas and remain clear.
If necessary, attempt to contact the Airfield Operations Dispatch (Station 3) and ask them to tell ATCT that you have cleared the movement area
Or, turn vehicle toward the Tower, flash headlights, and follow light gun signals.
Do NOT use a cell phone while on the movement area, unless it is an emergency and there is NO other way to contact anyone.
If the edge lights for the runway or taxiway you are on start flashing, the ATCT is attempting to contact you. Call them on the radio! If your radio is not working, turn your vehicle towards the ATCT, flash your headlights, and follow light gun signals.
If the aviation radio is malfunctioning, the vehicle must remain off the movement areas until the radio is repaired, or it must be escorted by a vehicle with an operating radio, operated by a trained and certified driver.
DTW
YIP
Radio Communications

## Slide 161
While on movement areas you must be escorted at ALL times by a trained and certified airfield driver who has a working aviation radio.
If you are separated from your escort, call them on the “county” radio and tell them you need help.
If you cannot contact your escort, call Airfield Operations on Ops 1 on the “county” radio and tell them you need help.
If that doesn’t work, flash your headlights at the Tower and follow light gun signals.
If you can’t contact anyone on the “county” radio, call Airfield Operations at 734-942-3685 and tell them you need help.
(using your cell phone is a last resort only!!!!!).
If the ATCT starts flashing light gun signals at you, obey them without entering a runway safety area, even if you have to drive onto a grassy area.
If an aircraft is moving towards you, get out of its way without entering a runway safety area (even if you have to go onto the grass).
ESA
Radio Communications

## Slide 162: Airfield Safety
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 163
Surface Incident
“Any event where unauthorized movement occurs
within the movement area
or an occurrence in the movement area
associated with the operation of an aircraft
that affects or could affect the safety of flight.”
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 164
Runway Incursion
“Any occurrence at an aerodrome
involving the incorrect presence
of an aircraft, vehicle or person
on the protected area of a surface designated for the landing and take-off of aircraft.”
A vehicle or person in a runway’s safety area is treated the same as if it is on the paved surface of the runway.
This means being inside the runway safety area
for an open runway
without prior authorization IS A RUNWAY INCURSION
even if there are NO aircraft operating on or near the runway!
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 165
Increasing Severity
Available
Reaction
Time
Evasive or
Corrective
Action
Category C
Separation decreases, but there is ample time and distance to avoid a potential collision.
Category B
Separation decreases and there is a significant potential for collision.
Category A
Separation decreases and participants take extreme action to narrowly avoid a collision.
Environmental
Conditions
Speed of
Aircraft and/or
Vehicle
Proximity of
Aircraft and/or
Vehicle
Little or no chance of collision, but meets the definition of a runway incursion.
Category D
Factors affecting the severity decisions of a Runway Incursion
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 166
Hot Spots
A “hot spot” is a location on the movement area with a high risk of collision or runway incursion, and where greater attention by pilots and drivers is necessary.
HS 1:
27R-9L @ 21R-3L (note runway stop bar lights
DTW
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 167
Runway Close/Open Procedures (DTW)
Procedures play vital role in preventing runway incursions.
Ensures everyone knows when runways close and open.
Procedures must be followed exactly in order to be effective.
ATCT closes runways – Airfield Ops opens them.
DTW
ESA
Runway Incursion Awareness and Airfield Safety
Initial – Rwy/Twy Opening/Closing Procedures handout
Notes: Have trainees pull out WCAA Ops document Runway/Taxiway Opening and Closing Procedures

## Slide 168
Closing Runways
    Ops receives notification from ATCT via phone that the runway is closed.
    Ops issues NOTAM.
    Ops updates Runway Status in Passur-Communicator to match NOTAM.
    Ops announces closing on WCAA radio channels Ops 1, Maint 1, and Maint 3.
    Ops notifies Flight Service via phone of runway status if NOTAM Manager is inoperative.
    On the airfield, confirmation should be obtained from ATCT that the runway is closed (hearing ATCT confirm it to another vehicle operator is acceptable).
DTW
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 169
Opening Runways
    An Ops Specialist is responsible for inspecting to ensure all persons and equipment are clear (normally the Runway Inspector for the day).
    Every group leader on the runway during the closure (Maint Foreman, Painter Foreman, Electrical Foreman, and any others) MUST contact the Runway Inspector via radio to advise that they and their people are clear of the runway.
    FAA Tech Ops calls clear by contacting Ops Dispatch or the Runway Inspector.
    Once clear, no one should re-enter the runway safety area without getting the OK from the Runway Inspector!
DTW
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 170
Opening Runways
    Runway Inspector inspects runway and associated safety areas.
    Runway Inspector advises Dispatch that runway can be opened.
    Ops announces opening on WCAA radio channels Ops 1, Maint 1, and Maint 3.
    Ops Dispatch and the Runway Inspector listen for acknowledgements from all personnel who were on the runway while it was closed.
    Ops updates NOTAM Manager.
    Ops updates Runway Status in Passur Communicator to mATCTh the NOTAM.
    Ops notifies Tower via phone that the runway is open.
    Ops notifies Lansing Flight Service if applicable.
DTW
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 171
Who do you contact if you see an unsafe condition on he airfield?
Reporting Unsafe Conditions
Review DTW YIP

## Slide 172
Reporting unsafe conditions
An “unsafe condition” could be wildlife activity, a speeding or careless driver, a vehicle accident, an unauthorized person on the movement area, something that just doesn’t look right, or more.
DTW:
  Contact ATCT or call Airfield Operations (Station 3).
  Persons who don’t have a “county” radio should call Ops Dispatch (but NOT while on a runway, taxiway, or taxilane), 734-942-3685.
YIP:
  contact ATCT or call Airfield Operations (Station 3).
  Persons who don’t have a “county” radio should call (but NOT while on a runway, taxiway, or taxilane) YIP Ops at 734-485-6675 or Ops Dispatch 734-942-3685.
DTW
YIP
Runway Incursion Awareness and Airfield Safety

## Slide 173
Reporting unsafe conditions
An “unsafe condition” could be wildlife activity, a speeding or careless driver, a vehicle accident, an unauthorized person on the movement area, something that just doesn’t look right, or more.
Contact a supervisor, call Airfield Operations (Station 3), or contact ATCT.
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 174
Situational awareness
Defined as “knowing what is going on so you can figure out what to do.”
Can be broken down with answers to the following questions:
  What is happening?
  Why is it happening?
  What could happen next?
  What am I going to do about it?
Another way to think of situational awareness while on the airfield:
  Being aware of one's surroundings…
  Identifying potential threats and dangerous situations…
  And doing something about them.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 175
Situational awareness
Two major characteristics of Situational Awareness:
  It is a mindset, not a skill.
  It is forward-thinking.
Some occupations that require good SA skills:
Flight crews (including flight attendants)
Law enforcement
Firefighters
EMS
Air traffic controllers
Sawyers (timber cutters)
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 176
Situational Awareness
Examples of factors that can cause you to lose SA:
  Complacency.
  Fixation on tasks.
  Pressure to hurry up and complete a task.
  Personal problems or other non-work events and situations that are on your mind.
What do all of these examples have in common?
They are DISTRACTIONS
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 177
Airfields have many different types of distractions:
Fog
Rain/Snow
Darkness/Glare
Obscured Pavement Markings
Obscured Lights and Signs
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 178
Situational Awareness
Name three types of distractions.
Review DTW YIP

## Slide 179
Types of Distractions
Visual – Distractions that take your eyes off your surroundings.
Physical – Distractions that take your hands off the steering wheel (if you are driving) or off the equipment you are operating.
Mental – Distractions that take your mind off what you are doing or where you are.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 180
Types of distractions
Nate Burleson (former Lions receiver) gave us a perfect example of all three types of distractions.
After a pizza promotional event, where he was given a couple of free pizzas, he was driving home on I-696.
This article tells what happened next (click on link):
"The Pizza Incident"
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 181
Types of distractions
Nate Burleson (former Lions receiver) gave us a perfect example of all three types of distractions.
Visual: took his eyes off the road.
Physical: took a hand off the steering wheel.
Mental: was more worried about a $10 pizza than his 2009 Yukon!
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 182
Establishing an effective SA mindset
Recognize that threats exist.
Take responsibility for one's own security.
Trust your "gut" or intuition.
Make a constant conscious effort to pay attention to your instincts and surrounding events even when you are busy.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 183
Consequences of Runway Incursions
The individual’s DTW Airport ID badge is immediately confiscated by WCAA.
The individual will not be allowed to re-enter the Airport Movement Area until the CEO receives a letter from the individual’s supervisor indicating that the individual has been counseled and has received recurrent company training.
The individual’s DTW Airport ID badge will not be returned until ground vehicle training and testing is conducted by the Airfield Operations Department.
Other discipline may be issued in accordance with individual company rules.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 184
Consequences of runway incursions
For WCAA employees, from the WCAA Employee Handbook:
  An employee who is found to be responsible for a Runway Incursion or other related misconduct in violation of FAR 139 will be subject to progressive discipline.
  In the event it is determined an employee has been involved in a runway incursion for a second time, termination of employment may be warranted.
  As with all discipline, the WCAA will take appropriate disciplinary action without regard to progressive discipline, when the offense is deemed to be serious in nature.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 185
The driver of this pickup truck, which was at the approach end of an open runway, saw a 747 on final approach.
He jumped out of the vehicle and ran.
The pilot reported feeling a “slight shudder” in the main gear just before landing.
Or Worse!
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 186
Two Boeing 747 jumbo jets collided head-on at the airport on Tenerife Island in 1977.
Because of fog, missed communications, and one pilot’s overconfidence and loss of situational awareness, one of the B-747's started its takeoff roll while the other was on the runway.
In the resulting collision, 583 people died.
For more details, read (click on link – skip if short on time):
The True Story Behind the Deadliest Air Disaster of All Time
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety

## Slide 187: Airfield Safety
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 188
What are some sources to check on the status of runways or the airfield in general?
Review DTW YIP
Airfield Safety and Runway Incursion Prevention
Best Practices
Notes: - ATIS – ATCT – Passur - Airfield Operations Dispatch (Station 3) - Lighted X (9L/27R) - Pilot Web

## Slide 189
Review current airfield information on Passur for any runways open/closed, taxiway closures, construction activity, or other surface risks.
For runway status:
  Check ATIS.
  Check Passur.
  Contact Airfield Operations Dispatch.
  Look for lighted “X” (Rwy 9L/27R at DTW).
  Check NOTAMs at Pilot Web https://pilotweb.nas.faa.gov/PilotWeb/
  Contact ATCT
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 190
For runway status:
  Contact your Manager/Foreman
  Check ATIS.
  Contact Airfield Operations Dispatch (Ops 1)
  Look for lighted “X” (Rwy 9L/27R at DTW).
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 191
Review and understand airfield signage and markings.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 192
If necessary, review the airport diagram prior to moving the vehicle.
Have the airport diagram out and available for immediate reference while driving in the operational area.
Use service and zipper roads whenever possible to minimize time spent on taxiways and runways.
If necessary, copy your clearance and review the assigned route. Read back all clearances.
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 193
Eliminate distractions while driving in the operational area. Do not use cell phones while driving in the operational area.
193
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 194
ESA
Hazardous locations and situations
Working on and around runways demands exceptionally high degrees of situational awareness.
Are there other airfield locations or situations that require high levels of situational awareness? Some examples:
  Performing routine tasks on an open surface (repairing a light, filling a hole, investigating a bird strike, retrieving FOD, etc).
  Vehicle escorts (fuel trucks, slow-moving vehicles, and vehicles where the operator has little to no situational awareness).
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 195
ESA
Hazardous locations and situations (continued)
Are there other airfield locations or situations that require high levels of situational awareness? (continued):
  Runway inspections.
  High air traffic activity (arrival and departure banks).
  Obscured or out-of-service airfield lights, signs, or markings.
  Blind spots (buildings or objects blocking your view of taxiways, taxilanes, aircraft gates, etc).
  Winter and low-visibility operations.
Can you think of other examples that are unique to your duties on the airfield?
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 196
ESA
Maintaining situational awareness
Situational awareness is a mindset and not a skill.
Developing that mindset is something you have to actively work at.
You want to get to the point where it’s something you do instinctively.
The following is adapted from “Cooper’s Color Codes.”
It was originally developed for self-defense training.
You can apply these codes to the airfield activities listed on the previous slide, and many more.
White | Totally complacent. Unaware, unprepared, and unready to take action.
Yellow | Prepared, alert, and relaxed. Good situational awareness.
Orange | Specific alert to probable danger. Ready to take action.
Red | Action mode. Totally committed to the emergency or hazard at hand.
Actively work at all times to identify potential hazards and change your mindset to the appropriate color code.
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 197
ESA
Maintaining situational awareness (continued)
What are some other ways to help you maintain good situational awareness?
Develop a mental checklist of situations and hazards that will cause you to instinctively move to a higher “color code.” Examples:
  Remind yourself to go to “yellow” when an AOA gate opens and you enter the AOA.
  Go to “orange” when you are on a taxiway or connector taxiway close to a runway.
  Go to “red” before driving on or crossing a runway.
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 198
ESA
Maintaining situational awareness (continued)
What are some other ways to help you maintain good situational awareness? (continued)
  Don’t stare at objects.
    Note their location, and direction and speed of travel if they are mobile.
    Develop a game plan to deal with them.
    Continue scanning.
  Regularly change your visual focus regularly from near to far.
  Think about what is not happening as well as what is happening.
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 199
ESA
Maintaining situational awareness (continued)
Develop personal safety habit patterns and learn to use them instinctively.
Anticipate by using an active thought process, don’t assume!
  “I’m approaching a runway. I anticipate that I’ll have to contact ATC to cross unless I verify that the runway is closed.”
Always drive with a slightly nervous edge.
“Is something or somebody out there trying to hurt or kill me?” Trust your “gut” or intuition (your “sixth sense”).
If you get that “hair on the back of the neck” feeling that something is wrong – pay attention to it and do something about it!
Recognize when you aren’t feeling 100% mentally or physically and compensate accordingly.
Sleepy bus driver hits Air India aircraft
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 200
During radio transmissions, use correct terminology, structure, and voice cadence.
STOP the vehicle on the taxiway and request ATCT clarification if there is confusion regarding your position or your clearance.
Ensure appropriate vehicle lights (high beams, flashers, beacons, and strobes) are operational prior to driving in the operational area. They help ATCT, aircrew and other vehicle operators see vehicles, especially during periods of reduced visibility and at night.
When cleared to cross any runway or taxiway, first visually check to ensure there is no conflicting traffic.
If there is any doubt that the runway is clear, reconfirm crossing clearance with ATCT.
DTW
YIP
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 201
Listen closely to the radio and maintain a “mental map” of aircraft movements.
Contact your Manager/Foreman if there is any confusion or questions about what you’re supposed to do or where you’re going. Especially important when a runway is involved!
Ensure appropriate vehicle lights (high beams, flashers, beacons, and strobes) are operational prior to driving in the operational area. They help ATCT, aircrew and other vehicle operators see vehicles, especially during periods of reduced visibility and at night.
When cleared to cross any runway or taxiway, first visually check to ensure there is no conflicting traffic. If there is any doubt that the runway is clear, contact the Manager or Foreman who is escorting you.
Focus attention and have your "eyes out" of the vehicle.
Maintain appropriate speed.
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 202
Focus attention and have your "eyes out" of the vehicle.
Maintain appropriate speed.
Be alert to similar aircraft and vehicle call signs operating on the field.
Know the Airport Layout
Follow established procedures
Never make assumptions while operating in the movement area
Read back all instructions verbatim.
Use all your senses (including your sixth sense) to maintain SITUATIONAL AWARENESS.
ASK QUESTIONS IF THINGS “JUST DON’T SEEM RIGHT!”
DTW
YIP
ESA
Runway Incursion Awareness and Airfield Safety
Best Practices

## Slide 203
Thank you!
WCAA Airfield Training Office
734-942-3595